## Slide 1: NERIS Topical Workshop on the Management of Contaminated Goods 22 May 2013 – CIEMAT - Madrid, Spain
V. Kutkov, E. Buglova, T. McKenna IEC/NS
International standards with regard to restriction/replacement of contaminated food, milk and drinking water in the accident State/affected States

## Slide 2: Introduction: Learning lessons

## Slide 3: Conceptual background for criteria
2007: ICRP-103
Protective strategy
Reference level of residual dose
The 2007 Recommendations of the International Commission on Radiological Protection (2007)
1990: ICRP-60
Single protective action
Action level of avertable dose
Notes: IAEA Training in Emergency Preparedness and Response
3

## Slide 4: Detectability of stochastic effects
278. "…further follow-up and improved information on the doses received will be needed before the shape of the dose response at low doses for both morbidity and mortality can be determined with confidence at doses below about 100-200 mSv.
[UNSCEAR Report 2000 Annex G: Biological effects at low radiation doses]
UNSCEAR Report 2010
UNSCEAR Report 2012

## Slide 5: Application of the effective dose
(153) The main and primary uses of effective dose in radiological protection for both occupational workers and the general public are:
  prospective dose assessment for planning and optimisation of protection; and
  retrospective dose assessment for demonstrating compliance with dose limits, or for comparing with dose constraints or reference levels.
(2007 Recommendations of the ICRP)

## Slide 6: Application of dosimetric quantities

## Slide 7: Human protection and safety
Safety
Protection

## Slide 8: Basic principles of protection strategy
All possible efforts should be made to prevent severe deterministic health effects and to reduce the occurrence of stochastic effects
A reference level expressed in terms of residual dose shall be set, typically an effective dose in the range 20–100 mSv, that includes dose contributions via all exposure pathways
The protection strategy shall include planning for residual doses to be as low as reasonably achievable below the reference level, and the strategy shall be optimized at preparedness stage

## Slide 9: General Safety Guide GSG-2
Criteria for Use in Preparedness and Response for a Nuclear or Radiological Emergencies: General Safety Guide No. GSG-2 (18 March 2011)
Jointly sponsored by the FAO, IAEA, ILO, PAHO, WHO
Published in En, Ar, Fr, Ru
Notes: .

## Slide 10: The new document in EPR Series
Actions to Protect the Public in an Emergency due to Severe Conditions at a Light Water Reactor
. EPR-NPP Public Protective Actions [2013]
Project started 18 March 2011
Fukushima Daiichi 11 March 2011
10
Notes: IAEA Training in Emergency Preparedness and Response
10

## Slide 11: Strategy to reduce the risk of stochastic effects: Generic Criteria
PROJECTED DOSE | PROTECTIVE STRATEGY | 
 | URGENT actions ► Dose in 7 DAYS | EARLY actions ► Dose in 1 YEAR
Total effective dose | 100 mSv | 100 mSv
Total equivalent dose in foetus or embryo | 100 mSv | 100 mSv
Committed equivalent dose in thyroid | 50 mSv | NA

## Slide 12: Ensuring safety of the public in emergency exposure situation
Reference level for public exposure during 1st year | 
10 mSv | Appendix IV. Generic criterion for food, milk and water to reduce the risk of stochastic effects in an emergency
Restriction/Replacement of contaminated food, milk and drinking water is one of components of URGENT and EARLY protective strategies together with sheltering, evacuation, relocation, decontamination, etc.

## Slide 13: Operational Interventional Levels
OILs – a predetermined default operational triggers for quantities that are measured by a field monitoring instrument or determined by laboratory analysis.
Protective and other response actions
Dose rate from skin contamination
Dose rate from thyroid
Dose rate above
the ground
Food and water concentrations
13

## Slide 14: Basis for development of foods’ OILs
Apply for the domestic use of foods in an emergency exposure situation
100% of the food, milk and water are initially contaminated due to ground deposition and are consumed for a full year
Intervention, natural weathering and dilution with a time are not concerned. Radionuclide concentration in foods decrease with a time due to decay only
Representative person – infant: 1 year old ICRP reference person consuming 500 kg per annum

## Slide 15: Control of radionuclides in foodstuffs at radiological emergency
OIL | RN | Activity concentration of single radionuclide in foodstuff | Implementation of protective actions
OIL6 | Cs-137 | 2000 Bq/kg | For the confirmation foodstuffs and drinking water restrictions
 | I-131 | 3000 Bq/kg | 
 | Sr-90 | 200 Bq/kg | 
 | Pu-239 | 50 Bq/kg | 

## Slide 16: Emergency exposure situation
1986
2011
UNKNOWN SOURCE TERM
16
Notes: IAEA Training in Emergency Preparedness and Response
16

## Slide 17: Fukushima test case
17
17
Notes: IAEA Training in Emergency Preparedness and Response
17
Workshop on Expanded Response in Nuclear Emergencies
Module L-ER-9. Sources and Pathways of Public Exposure in Emergency

## Slide 18: Generic and operational criteria

## Slide 19: Size of the emergency zones and distances
Emergency zones and distances | Power ≥ 1000 MW(th) | Power ≥ 100 to 1000 MW(th)
PAZ: Precautionary action zone | 3 to 5 km | 
UPZ: Urgent protective action planning zone | 15 to 30 km | 
EPD: Early action planning distance | 100 km | 50 km
FRD:Ingestion and commodities planning distance | 300 km | 100 km
19
Notes: IAEA Training in Emergency Preparedness and Response
19

## Slide 20: Control of alimentary pathway at Urgent phase if NPP emergency
20

## Slide 21: Pathways considered in calculation of OIL3 and OIL7
21

## Slide 22: Control of radionuclides in foodstuffs at NPP emergency
OIL | Default value | Assessed monitoring result | Implementation of urgent actions
OIL3 | 1 μSv/h | Ambient dose rate at 1 m above ground level | For initial foodstuffs and drinking water restrictions
OIL7 | 1000 Bq/kg | Concentration of marker I-131 in foods | For the confirmation and/or extension of initial foodstuffs and drinking water restrictions
 | 200 Bq/kg | Concentration of marker Cs-137 in foods | 

## Slide 23: Summary: from GS-R-2 to GSR Part 7
Introduction of the new dose concepts, dosimetric quantities and criteria
    Generic and operational criteria of projected dose for protective and other actions to avoid or minimize severe deterministic effects
    Generic and operational criteria of projected dose for protective actions corresponding to the reference levels of residual dose to reduce risk of stochastic effects
23

## Slide 24: Any questions?