## Slide 1: The Advanced Source Inversion Module of JRODOS
S. Andronopoulos1, I. Kovalets2,3, O. Pylypenko2,3, D. Treebushny4, R. Hofman5, P. Seibert5, I. Ievdin3,6
1NCSR Demokritos, Institute of Nuclear and Radiological Sciences and Technology, Energy and Safety, Agia Paraskevi, Greece
2Institute of Mathematical Machines and Systems Problems NAS of Ukraine, Kiev, Ukraine
3Ukrainian Center of Environmental and Water Projects, Kiev, Ukraine
4Karlsruhe Institute of Technology, Karlsruhe, Germany
5University of Vienna, Austria
6BfS—Federal Office for Radiation Protection, Oberschleissheim, Germany

## Slide 2: Some background information
Source-Inversion Advanced module developed and firstly integrated in JRODOS by the PREPARE project
  Estimation of time-dependent emission rate and nuclide composition from a NPP accident, based on gamma dose-rate (GDR) measurements (top-down approach)
  Methodology based on minimization of a cost function using “Source-Receptor Functions” (SRF) formulated on the ADM DIPCOT

## Slide 3: Purpose of presentation
Dissemination of testing of JRODOS-integrated SIA
Methodology:
  Hypothetical NPP accident with a defined “true” source term
  Artificial GDR measurements by running ADM
  Assume a first-guess source term
  Run the SIA and examine closeness of the estimated source term to the true one

## Slide 4: Test-case definition
Hypothetical accident at Rivne NPP (Ukraine)
Source term F1.DRSA-FK1 (JRODOS database)
  27 nuclides: noble gases, iodines, aerosols particularly challenging case

## Slide 5: Measurements
Artificial GDR measurements generated by DIPCOT at artificial sensors around the NPP
Distances of sensors from the NPP: 8-30 km
Artificial meteorology: time-varying wind direction, constant wind speed, D-stability, no precipitation

## Slide 6: Measurements (cont’d)
“Measurements” imported in JRODOS database

## Slide 7: SIA parameters
Control the calculation of regularization terms
They affect the SIA method performance
What are the optimal values?
“alpha_sigmab”:
  Determines how closely the SIA converges to the first-guess (background) source term

## Slide 8: What is the optimal value?
Run the SIA (calculate the source term) for several values of
For each source term calculate the Mean Absolute Error between observed and model-calculated GDR:
Plot the curve
The optimal value is where the curve presents the maximum curvature (L-curve approach)  optimal estimated source term

## Slide 9: 1st test
First-guess source term equal to 1/10th of the true one
Optimal

## Slide 10: 1st test – results – total releases

## Slide 11: 1st test – results – split

## Slide 12: 2nd test
First-guess source term equal to 10 times the true one
Optimal

## Slide 13: 2nd test – results – total releases

## Slide 14: 2nd test – results – split

## Slide 15: 3rd test
First-guess source term equal to true one but shifted in time 1 hr forward

## Slide 16: 3rd test – optimal
Optimal

## Slide 17: 3rd test – results – total releases

## Slide 18: 3rd test – results – timing

## Slide 19: 4th test
First guess source term: increased by 10 times during 1st half of release, decreased by 10 times during 2nd half, in relation to true one

## Slide 20: 4th test -optimal
Optimal

## Slide 21: 4th test – results – total releases

## Slide 22: 4th test – results – split

## Slide 23: Conclusions
In all simulated cases the estimated time-dependent source term was closer to the true one than the first guess
The level of improvement varied between cases
  Test 1: estimated releases of aerosols and noble gases within a factor of 1.5 as compared to the true values; iodine release estimation not improved

## Slide 24: Conclusions (cont’d)
  Test 2: estimated releases of all nuclide groups within a factor of 2 to 5 compared to true values (modest improvement)
  Test 3: timing of releases estimated correctly; magnitude of releases estimated within a factor of 1.5 to 2 compared to true values (“best” case)
  Test 4: estimated releases improved; estimated ST RMSE = 1.05×1015 Bq/s; first-guess ST RMSE = 4.09×1015 Bq/s (“worst” case)
Future work: calculation of optimal values of parameters; unknown location of release

## Slide 25: References
I. Kovalets, I. Ievdin, R. Hofman, P. Seibert, S. Andronopoulos (2016) “Description of software module for source term estimation using advanced method integrated in DSS RODOS”, Report PREPARE(WP4)- (16)-04
Kovalets I. , Andronopoulos S., Hofman R. , Seibert P., Ievdin I. (2016) “Advanced method for source term estimation and status of its integration in JRODOS”. Radioprotection 51 HS2, S121-S124, doi:10.1051/radiopro/2016046
Kovalets I., Andronopoulos S., Hofman R., Seibert P., Ievdin I., Pylypenko O. (2018) “Advanced Source Inversion Module of the JRODOS System”. In: Agarwal R., Agarwal A., Gupta T., Sharma N. (eds) Pollutants from Energy Sources. Energy, Environment, and Sustainability. Springer, Singapore. pp 149-186 DOI: https://doi.org/10.1007/978-981-13-3281-4_10

## Slide 26
Thank you very much for your attention!