## Slide 1: Decision support diagrams for public protective actions during nuclear emergencies 5th NERIS Workshop, 3-5 April 2019
Jan Johansson, Peder Kock, Anna Maria Blixt Buhr, Jonas Lindgren, Jonas Boson, Simon Karlsson

## Slide 2: Responsibilities during nuclear emergencies
Decision making
  Decision making rests with the organisations normally responsible for the sector or the administrative region
  The County Administrative Boards are responsible for decisions on civil protection (e.g. evacuation and sheltering)
Advice
  SSM is responsible for providing recommendations and expert advice on i.a. protective actions, dispersion prognosis, radiation monitoring and conditions at the NPP
Licensee
  A licensee is required to take prompt actions in order to classify the event, alert authorities, assess possible releases and restore the facility to a safe and stable state

## Slide 3: Prerequisites
Based on emergency class and estimated release magnitude
Adapted to the possibilities for protective actions offered by the present emergency response planning
Covers an event from facility emergency to termination of the emergency
Decisions on protective actions primarily at predetermined distances
Some protective actions to be implemented all around the NPP whereas others within the area at risk
High threshold to terminate decided protective actions

## Slide 4: Protective actions
Precautionary evacuation
Evacuation
Sheltering
ITB
Relocation
Actions to reduce inadvertent ingestion of radioactive substances on the skin
Decontamination of people
Medical care
Food restrictions

## Slide 5: Release magnitude
Release magnitude | Xe-133 | I-131 | Cs-137
FMS1 | ~5E+18 Bq | ~1E+15 Bq | ~1E+14 Bq
10xFMS1 | ~5E+18 Bq | ~1E+16 Bq | ~1E+15 Bq
100xFMS1 | ~5E+18 Bq | ~1E+17 Bq | ~1E+16 Bq
1FMS stands for ”Functioning Mitigation Systems” where the release corresponds to the requirements on mitigation systems in a governmental decision from 1986
Influences distances where protective actions are implemented

## Slide 6: Objective for protective actions
Protective action | Less than FMS | Between FMS and 10xFMS | Between 10xFMS and 100xFMS
Evacuation1 | 0-5 km | 0-15 km | 0-152 km
Sheltering | 5-15 km | 15-25 km | 15-50 km
ITB | 5-15 km | 15-253 km | 15-503 km
1Both precautionary evacuation and evacuation
2Evacuation out to 25 km can be considered in sectors without larges communities
3Additional distribution of ITB is required

## Slide 7: Time to and duration of release
Time to release
  Influences the area affected by the release
  Influences if complementary and additional ITB can be distributed
  Influences when to recommend sheltering
  Influences when to recommend intake of ITB
  Influences when to recommend food restrictions
Duration of release
  Influences the area affected by the release
  Influences when sheltering can/must be discontinued

## Slide 8: Area at risk and adjustment of distances
Area at risk
  Area that may be affected by a release to such an extent that protective actions are necessary
  Area at risk can cover certain sectors or the full circle around the NPP
Adjustment of distances
  Distances for evacuation, sheltering and ITB may be adjusted based on the actual weather situation
  Adjusted distances based on dispersion prognosis and present release magnitude FMS, 10xFMS or 100xFMS

## Slide 9
Questions?
Contact: jan.johansson@ssm.se