## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Emergency preparedness for long lasting releases – Overview
STUK, Finland: T. Peltonen
VUJE, Slovak Republic: A. Bujan, T. Duranova, J. Duran, L. Bohun
CIEMAT, Spain: M. Montero, C. Trueba
KWR, KNMI, RIVM, The Netherlands: L. Puijker, H. de Vries, C. Twenhöfel
BfS, Germany: F. Gering, K. Arnold, B. Gerich
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 2: WP1: Review of emergency preparedness for long lasting releases
Objectives In all countries with nuclear installations detailed emergency management strategies have been developed in the past. In nearly all cases such strategies are based on accident scenarios where the duration of the release of radionuclides to the environment is limited to some hours or at maximum a few days. The Fukushima accident has demonstrated the possibility of long-lasting releases of radionuclides from a nuclear power plant over several weeks. The overall objective of this work package is to test the current off-site nuclear emergency planning in European countries with accident scenarios based on lessons learned from the Fukushima accident and to derive recommendations how to improve the current planning. The tests should demonstrate whether protective measures foreseen in the current emergency planning could adequately reduce the radiological consequences of NPP accidents with long lasting severe releases similar to the release from the Fukushima-Daiichi NPP. Results of that WP will be input for the knowledge data bases of WP2

## Slide 3: Presentation of WP1 results
Source terms (WP 1.1) – presented by Albert Bujan, VUJE: Investigation of hypothetical source terms leading to long-lasting releases of radionuclides and which are applicable to nuclear installations in various European countries.
Weather scenarios (WP 1.2) – presented by Milagros Montero Prieto, CIEMAT: Development of accident scenarios for nuclear installations in European countries based on source terms resulting from WP 1.1 and typical weather scenarios for various nuclear installations in Europe.
Assessment of radiological consequences (WP 1.3) – presented by Tuomas Peltonen, STUK: Assessment of off-site radiological consequences of accident scenarios resulting from WP 1.2. The assessment includes a detailed modelling of atmospheric transport of radionuclides and an detailed assessment of the radiological consequences.

## Slide 4: Outline
Impact on drinking water and uncertainty assessment – presented by Leo Puijker, KWR and Hans de Vries, KNMI: Impact of a Fukushima-like release in the Netherlands on drinking water and probabalistic assessment of the affected sectors.
Conclusions for Emergency Preparedness and Response for long lasting releases – presented by Florian Gering, BfS: Evaluation of current off-site nuclear emergency planning in various countries in Europe based on the results from WP 1.3

## Slide 6
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Conclusions for Emergency Planning and Response for long lasting releases
STUK, Finland: T. Peltonen
VUJE, Slovak Republic: A. Bujan, T. Duranova, J. Duran, L. Bohun
CIEMAT, Spain: M. Montero, C. Trueba
KWR, KNMI, RIVM, The Netherlands: L. Puijker, H. de Vries, C. Twenhöfel
BfS, Germany: F. Gering, K. Arnold, B. Gerich
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 7: Conclusions: Approach
Approach:
  Consequence assessment with decision support systems based on representative source terms
  Assessment for many accident scenarios (46-365 weather scenarios per ST)
  Analysis of the results by comparing against intervention criteria
Similar to the IAEA approach as proposed in: EPR-NPP PUBLIC PROTECTIVE ACTIONS [2013]
4 quite different approaches (7 NPP’s in 4 countries) provided a good basis for the evaluation of radiological consequences
In every country there were
  different long-lasting source terms (22-188 Hours, 3-600 PBq I-131)
  different weather scenarios
  different atmospheric dispersion models
=> Wide range of results
Nevertheless, the selected approach proved to be a valuable tool for evaluating the applicability of current EPR concepts also for long-lasting releases

## Slide 8: Conclusions: Max. distances for PA
Are the current emergency planning zones sufficiently reflecting the potential radiological impact of long-lasting releases?
Spain: The areas for protective actions do not exceed the limits of current planning zones (10 km, Zone I).
Finland:
The areas for evacuation and sheltering quite rarely exceed the emergency planning zones. In the cases where these distances are exceeded, the amount of affected population remains quite small.

## Slide 9: Conclusions: Max. distances for PA (2)
Are the current emergency planning zones sufficiently reflecting the potential radiological impact of long-lasting releases?
Slovak Republic: The areas for protective actions do not exceed the limits of current planning zones.

## Slide 10: Conclusions: Max. distances for PA (3)
Maximum distance for evacuation
Release over 15 days
Release over 2 days
Maximum distance for evacuation
Cumulative frequency
Cumulative frequency
While affected areas are getting larger with increasing release duration, the maximum distances for protective actions are decreasing

## Slide 11: Conclusions: Sectors affected
Is the current concept of emergency planning zones as being implemented in various countries reasonably applicable for long lasting releases?
Spain: In most cases not more than 4 sectors (≤90°) are affected
Finland: In most cases not more than 3 sectors (≤90°) are affected for evacuation and sheltering, but more for partial sheltering and ITB for children

## Slide 12: Conclusions: Sectors affected (2)
Cumulatice sector coverage for different release times:
The number of sectors in the 5 and 20 km zones around the release point, where actions have to be taken, will increase when the release continues in time, depending on the changes in the wind direction.
=> 90°-zones are only sufficient for releases < 24 hours
German evacuation concept:

## Slide 13: Conclusions: Intervention criteria
Are current intervention criteria appropriate for long lasting releases?
According to this assessment the intervention criteria (in Nordic countries) seem to be appropriate also for these kinds of long-lasting releases. As the considered scenarios were severe INES level 7 accidents (for Finland), it can be assumed that the criteria are suitable for less severe scenarios also.
There may be problems in the implementation of protective measures in the short term, since the release time can exceed even the stipulated time to determine the need for evacuation or temporary relocation.
In case of long lasting severe releases the critical situation can occur, that intervention criteria for protective actions are not exceeded in any 7-day-interval (for which some of the reference levels are currently defined in Germany), but the total dose over the release period by far exceeds the reference level.

## Slide 14: Conclusions: ICRP reference level
ICRP reference level for residual dose (over 1 year)
Spain: Areas where the upper ICRP reference level of 100 mSv (red areas) is exceeded are limited to <10 km zone
The current German intervention criteria are consistent with the new reference level for residual dose of 100 mSv (ICRP, EU BSS).
Protection strategy: Evacuation, sheltering, ITB, relocation after 30 days:
The residual dose over 1 year is:
always below 100 mSv
in about 1/3 of all cases higher than 50 mSv

## Slide 15: Conclusions: Implementation of PA
For very long lasting releases inside the EPZ sheltering indoors is probably not as suitable as in cases of a short release.
In case of long lasting severe releases the protective action “sheltering” may impose additional problems (e.g. the danger of being forced to order late evacuation even during passage of the plume, lifting of sheltering in one area while ordering in an another area), which endangers the applicability of the action in general.
In case of long lasting severe releases an one-time intake of stable iodine often is not sufficient for protecting the population against large thyroid doses. Multiple intake of stable iodine tablets may not be sufficiently considered in emergency planning.

## Slide 16: Conclusions: Drinking water
In case of a nuclear accident surface water can be contaminated by high levels of radionuclides and is not suitable for drinking water production
Common water treatment processes as aeration and filtration do not effectively remove I-131 and Cs-137
Advanced treatment processes as ion-exchange and reversed osmosis do remove radionuclides effectively, but these are not common practice
Soil passage (dune infiltration, river bank filtration, groundwater) are a safe barrier for I-131 and Cs-137
If surface water is the main direct source for drinking water production, emergency plans for drinking water supply are needed
Drinking water utilities in the European countries are required by the EU Drinking Water Directive to provide emergency drinking water in case of a major accident, including nuclear accidents

## Slide 17: Conclusions: Further remarks
Finland:
Two different numerical weather prediction (NWP) data models were used. However, they produce different results. In the case of NPP Olkiluoto the results are almost same. In the case of NPP Loviisa some results differ quite a lot. It has to be noted that also the selection of NWP model affects the results and is one source of uncertainty for radiological consequence assessments.
In this study only protection of people in the early phase of an accident was considered (exception: ICRP reference level). Other effects - including long-term effects, effects on biota including marine environment etc. - are also important issues when assessing the consequences of nuclear accident.
Finland:
The intervention criterion for partial shetering and ITB for children occurs naturally more often (due to low intervention criteria). The amount of population affected is highly dependent on dispersion direction.
During partial sheltering indoors it is recommended not to spend time outdoors unnecessarily. Such a protective action is much easier to recommend than totally sheltering indoors.

## Slide 18: What we have not done … (future work?)
Compare guidance related to lifting of countermeasures in different countries and – if existing! – check for applicability for long-lasting releases
Investigate effect of long-lasting emissions on monitoring strategies and capabilities
  Conversion of release rates to measureable quantities (dose rates, air concentrations) to study preparedness related to monitoring
  A long lasting low release rate of atmospheric discharge would probably require a very large capacity in air-sampling monitoring
  Identification of possible problems related to quantification of deposition during (residual) release
Study relative influence of peak releases and long lasting (residual) low release rate discharges to total impact and protection strategies
Check implementation of EU BSS (in different countries) on suitability for long-lasting releases
Is evacuation during passage of the plume nearly always preferable against sheltering (as stated in IAEA EPR 2013)?

## Slide 19
Thanks for your attention!
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].