## Slide 1: Review of emergency preparedness for long lasting releases Accident Scenarios
Milagros Montero; Cristina Trueba (CIEMAT)

## Slide 2: Working Team
PREPARE WP1.2 Team:
  Florian Gering, K. Arnold, B. Gerich BfS (Gremany)
  Tatiana Ďúranová, A. Bujan, J. Duran, L. Bohun . VUJE (Slovak Republic)
  Milagros Montero, Cristina Trueba CIEMAT (Spain)
  T. Peltonen STUK (Finland)

## Slide 3: Scope and Objectives
To test the current off-site nuclear emergency planning along Europe and to derive recommendations on how to improve it, two objectives have been followed:
  1º - to evaluate, using realistic scenarios, the consequences of accidents with long-lasting releases of radionuclides, according to the type of reactor involved and the varying conditions that influence the pattern of dispersion and deposition of radioactive contamination;
  2º - to explore whether these effects can be reduced and properly managed with the strategies and procedures currently planned.
A statistical study has been proposed by using potential long lasting release scenarios in combination with different weather conditions over a significant period of time (for instance one year) in some selected locations.
The results obtained in the development of accidental scenarios based in severe nuclear events with long lasting releases for a range of meteorological conditions representatives in the European countries, Germany, Slovakia, Finland and Spain, are presented.

## Slide 4: Methodology
Elements taken into account:
  The location of NPP, determines the zone potentially affected and the characteristics (topography, land cover, agricultural production, population, etc.) that may influence both the pattern of contamination and the radiological consequences
  The source term (ST), determines timing and magnitude of radioactive release to environment according to the type of reactor (in previous presentation)
  The weather conditions, determines the variability of dispersion and deposition of radioactive contamination. Two approaches:
    Typical weather scenarios derived from historical data from continuous monitoring of meteorological parameters at nuclear power plants.
    Specific scenarios selected from numerical weather predictions (NWP) for various locations of nuclear power plants in Europe, with calculation purposes.
A set of accident scenarios for each site has been derived by combination of:
N(ST/NPP)*N(Time periods)*N(NWPapproach)*N(MeteoDataset)

## Slide 5: Location of sites
  NPP Unterweser: in the north of Germany, very close to the coast, flat terrain. (1xPWR)
  NPP Grohnde: site in the middle of Germany, moderately structured terrain. (1xPWR)
  NPP Philippsburg: in the south of Germany in the Rhine Valley, surrounded by structured terrain (1xBWR / 1xPWR)
  NPP Mochovce: in the southwest of Slovakia, between the towns of Nitra and Levice (4xVVER-440/V213)
  NPP Loviisa: on the south coast (Gulf of Finland) (2xVVER-440 PWR)
  NPP Olkiluoto: on the west (Gulf of Bothnia) coast (2xBWR / 1xPWR )
  NPP Ascó: in northwest of Spain, in the Ribera d'Ebre area (Tarragona). (2xPWR)
Notes: In the south of Slovakia, between the towns of Nitra and Levice, there are located four VVER 440/V-213 pressurised water reactors units of the Mochovce NPP.

## Slide 6: Weather conditions – German NPP’s
Typical weather scenarios from a study with measurement data (2008-2012) available from these NPP sites
  Meteorological conditions, as stability class, wind speed and wind direction and the monthly mean values for precipitation, present distribution with strong deviations among the sites, but stable in each site along years.
  The selection of sites:
    Broad representation of all German NPPs
    The specific conditions at each site can be properly represented with a data set for an annual period
A NWP data set with 365 daily meteorological situations in each site for the statistical study has been selected.
Stability class, wind speed and wind direction

## Slide 7: Weather conditions – Slovakian NPP’s
Typical dispersion conditions from monitoring data (1981 – 2010). Meteorological pattern:
  with typical annual and daily temperatures cycle, influenced by Mediterranean and Eurasian continent and affected by the global warming,
  precipitations with double annual rainfall course,
  a predominance of stability class D
  prevailing winds in directions NW (29%), E (19%), and SE (18%) with moderated speed
The set of 144 meteorological conditions obtained from the real meteorological hourly data in the year 2010 is used with meteorological conditions for the assumed accident with an accident conditions stored in the source term file STC10-8d.

## Slide 8: Weather conditions – Finnish NPP’s
From statistical analyses of monitoring data (~9 years for Loviisa, ~5 years for Olkiluoto ):
  Wind roses represent the typical wind conditions of both sites.
  As they are located at coastal area >> influence of sea breeze (April to August) on dispersion conditions
To obtain the accident scenarios, FMI produces particle trajectories from NWP of HIRLAM and ECMWF models used.
  A data set of 40 meteorological conditions has been obtained for each site. Four different one week periods, with interval of 3 months to get seasonal variation. In each period a data set of five days with variable start times are selected.
Notes: European Centre for Medium-Range Weather Forecasts (ECMWF)

## Slide 9: Weather conditions – Spanish NPP’s
From the local meteorology studies (1975-1999) conducted in the safety evaluation of Ascó NPP the annual rose shows a strong directional influence of topography, prevailing winds clearly aligned with the direction of the valley, SSE and NNW:
  The highest frequency in the direction SSE (19.17%)
  Slightly lower frequency in the direction WNW (15.06%).
  Marked seasonal differences, with extremes cases in summer and winter
Selection weather scenarios according the seasonality: one month per season (January and July 2012), 46 datasets

## Slide 10: Summary of accidental scenarios
The main characteristics of these weather scenarios are the following:
  Weather scenarios are provided for seven NPP’s in four countries.
  The data includes both numerical weather predictions and on-site monitoring data.
  The statistical studies of monitoring data are usually to define typical or extreme meteorological situations, differ substantially regarding time periods covered (4 to 24 y) and time resolutions (10 min to monthly mean values).
  The scenarios based on numerical weather predictions mainly differ regarding the time periods covered (1 month to one year) with range from a few representative weather scenarios for summer and winter for the NPP Ascó (46) to a broader range of 365 scenarios (for every day of a year) per ST, for the German NPPs.
  The combination of the weather scenarios with the ST‘s, results in a significant number of accident scenarios that can represent the variety of conditions for these severe events with long-lasting releases along Europe in order to undertake the subsequent statistical study on the consequences of these accidents.

## Slide 11: Thanks for your attention!!