## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Radiological Consequence Assessment
Tuomas Peltonen
STUK – Radiation and Nuclear Safety Authority, Finland
With Contributions from
BfS: F. Gering, K. Arnold
VUJE: T. Duranova, A. Bujan, J. Duran, L. Bohun
CIEMAT: M. Montero, C. Trueba
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 2: Outline
Introduction
Atmospheric Dispersion Modelling
Intervention Levels
Result Examples
Conclusions

## Slide 3: Introduction
In the PREPARE work package 1.3 there was carried out the assessment the off-site radiological consequences
The assessments were based on
  Source terms from WP 1.1
  Accident scenarios from WP 1.2
The assessment consisted of a detailed modelling of atmospheric transport of radionuclides and a detailed assessment of the radiological consequences, considering all relevant exposure pathways
Four institutions from different countries participated in radiological consequence assessment
  Bfs (Germany), STUK (Finland), VUJE (Slovak Republic), and CIEMAT (Spain)

## Slide 4: Introduction
Each partner selected some source terms from WP 1.1 results with appropriate weather datasets from WP 1.2 results
The atmospheric transport calculations were performed and results were presented in the context of national intervention levels
Results in different countries differ in
  Atmospheric dispersion model
  National intervention levels
  NPP location
  Source term
  Numerical weather date

## Slide 5: Atmospheric Dispersion Modelling: BfS
Software: RODOS (Linux)
Several severe releases (INES 5, 6 and 7)
3 NPP’s
Real weather data from 2012
4000 single simulations
Further statistical analysis based on simulations

## Slide 6: Atmospheric Dispersion Modelling: STUK
Dose assessment model VALMA
Weather data provided by Finnish Meteorological Institute (FMI)
Two different NWP models: HIRLAM and ECMWF
Calculation duration was 72 h with 0.5 hour time resolution
NPP sites Loviisa and Olkiluoto
  Treated as separate cases (different source terms)
In total 80 calculations.

## Slide 7: Atmospheric Dispersion Modelling: VUJE
Accident scenario for the Slovak NPP Mochovce
Atmospheric transport calculations were performed with RTARC operational atmospheric transport model
Annual meteorological conditions from SHMU measured data in the year 2010
Statistical processing and presentation of these data in a form of mean value, 5% and 95% percentile guarantee
Chart: Distance from NPP exceeded [km]
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | > 40
0 | 1
100
200
300
400
500
600 | 1
700 | 6 | 1
800 | 5 | 1
900 | 9
1000 | 7 | 3
1100 | 12 | 4

## Slide 8: Atmospheric Dispersion Modelling: CIEMAT
Two scenarios, winter and summer
One source term for NPP site Ascó
In total 46 calculations
Atmospheric dispersion modelling
  JRODOS / RIMPUFF
  98 hour prognosis
  NOMADS NWP

## Slide 9: Intervention Levels: Germany

## Slide 10: Intervention Levels: Finland (Nordic)

## Slide 11: Intervention Levels: Slovak Republic

## Slide 12: Intervention Levels: Spain
Protective actions | Generic Intervention Level (effective dose avertable)
Urgent Protective Actions - Early phase of an emergency | 
Sheltering | 10 mSv in 2 days.
Iodine prophylaxis | 100 mSv to the thyroid (equivalent dose)
Evacuation | 50 mSv in 7 days
Longer Term Protective Actions - Intermediate / late phases of an emergency | 
Temporary relocation | 30 mSv in first month and 10 mSv in a subsequent month. Return when averted dose < 10 mSv
Permanent resettlement | >10 mSv within 1 or 2 years (≈ 100 mSv / 1y) or >1 Sv in lifetime

## Slide 13: Result Example: BfS

## Slide 14: Result Example: STUK
Iodine in inhaled air is or is anticipated to exceed 10 000 Bq/m3 and 1 000 Bq/m3 respectively after 48 h

## Slide 15: Result Example: VUJE
Chart: Distances from the NPP where the optimal values of intervention levels for iodine prophylaxis are exceeded (scenario STC10-8d; IL = 100 mSv)
| 0.5 | 1 | 2 | 4 | 6 | 8 | 10 | 16 | 24 | 48 | 168
100 mSv - mean | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.7711 | 9.7205 | 10.525 | 11.0705
100 mSv - 5% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.2584 | 3.5576 | 3.5618
100 mSv - 95% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.825 | 22.2587 | 27.8612 | 31.0814

## Slide 16: Result example: CIEMAT

## Slide 17: The Effect of Weather Provider (STUK)
Intervention Criterion | Quantity | Avg (ECMWF) | Std (ECMWF) | Avg (HIRLAM) | Std (HIRLAM)
Total deposition of strong gamma and beta emitters is higher than 10 000 kBq/m2 | Area | 122 | 108 | 92 | 75
 | Distance | 14360 | 9046 | 14121 | 8746
 | Population | 593 | 734 | 464 | 460
External dose rate is exceeding 100 μSv/h | Area | 112 | 151 | 76 | 103
 | Distance | 9471 | 8742 | 6753 | 7675
 | Population | 400 | 660 | 546 | 1499
External dose rate is exceeding 10 μSv/h | Area | 2402 | 2165 | 1786 | 1892
 | Distance | 89368 | 30891 | 66971 | 22712
 | Population | 136647 | 278089 | 79089 | 157043

## Slide 18: Conclusions
Four quite a different approaches provided a good basis for the evaluation assessment of radiological consequences
In every country there was
  different long-lasting source term
  different weather scenario
  different atmospheric dispersion model
=> Very wide range of results
The whole work described in detail in deliverables
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].