## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Particles deposition modelling in atmospheric dispersion models of JRODOS
S. Andronopoulos
NCSR Demokritos
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 2: Introduction
Deposition of particles – dry and wet – depends – in addition to the factors affecting that of gases – on:
  Size
  Density
Until now deposition of particles in JRODOS is treated in the same way as that of gases
Observational evidence – presented in other tasks of WP4 of PREPARE – reveals that size and density of particles may be important to take into account – especially for large fuel particles
Therefore it was decided to implement a more detailed computation of particles dry and wet deposition in atmospheric dispersion models of JRODOS
  Taking into account the recommendations by other tasks of WP4

## Slide 3: Formulation – Dry deposition
Dry deposition flux Fd of particles to the ground is modelled through a “dry deposition velocity”:
depends on particle size
Partition to a specified number of size bins – each size bin characterised by a aerodynamic diameter – and taking a weighted average: ,
Difference with gases:
  settling velocity - depends on particle size and density
  deposition layer resistance

## Slide 4: Formulation: wet deposition
Wet deposition flux Fw of particles to the ground is modelled through a “wet deposition velocity”:
, Λ being the “washout coefficient”, H the height over which scavenging of the plume is taking place
Assumptions in JRODOS: uniform Λ over plume height, no distinction between in-cloud and below-cloud scavenging
Dependence of Λ on particle size and rain rate, according to Baklanov and Sørensen (2001)
, for μm
, for
, for
With , q being rain rate in mm/h
Weighted average of Λ for all size bins

## Slide 5: Assumptions for realization in JRODOS
Maximum 5 size bins – taking into account recommendations from other tasks and real-time operation requirements
All nuclides / species share the same partitions / size bins / densities
The properties are read from a simple ASCII file: number of bins, diameter for each bin, density for each bin, fraction in each bin
Dry deposition velocity is calculated in LSMC – update of existing subroutines – to be common for all dispersion models.
Washout coefficients are calculated in dispersion models

## Slide 6: Test results – DIPCOT in JRODOS
Dry deposition of particles, older scheme
Dry deposition of particles, newer scheme

## Slide 7: Test results – DIPCOT in JRODOS
Time-integrated concentration, older particles dry deposition scheme
Time-integrated concentration, newer particles dry deposition scheme

## Slide 8: Test results – DIPCOT in JRODOS
Ground gamma dose effective, older particles dry deposition scheme
Ground gamma dose effective, newer particles dry deposition scheme

## Slide 9: Test results – DIPCOT in JRODOS
Newer particles dry deposition scheme, effect of particle size
Upper: smaller particles (1μm)
Lower: larger particles (20μm)

## Slide 10: Test results – DIPCOT in JRODOS
Newer particles dry deposition scheme, effect of particle density
Upper: lower density particles (1 gr/cm3)
Lower: higher density particles (5 gr/cm3)

## Slide 11: Test results – DIPCOT in JRODOS
Wet deposition of particles, older scheme
Wet deposition of particles, newer scheme

## Slide 12: Conclusions
New dry and wet deposition schemes for particles have been implemented and tested
There is a clear effect on ground contamination
More noticeable effect from particles density
No noticeable effect on model running time

## Slide 13
Thank you for your attention
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].