## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Dispersion and fall out of particles larger and heavier than aerosols
Poul Astrup
Department of Wind Energy
Technical University of Denmark
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark
The research leading to these results has received funding from the
European Atomic Energy Community Seventh Framework Programme FP7/2012 under grant agreement no. 323287.

## Slide 2
Puff, definition:
A finite amount of material mixed into the air
Concentration distribution [material/m3] being Gaussian
Point of maximum concentration called the puff center
The standard deviation called the puff size.
Puff growth
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 3
Puff models for heavy particle dispersion
G.T. Csanady (1963): "Turbulent Diffusion of Heavy Particles in
the Atmosphere"
P. Astrup (2016): "Atmospheric dispersion of particles larger and
heavier than aerosols"
Particle models for heavy particle dispersion
Many, many, many, …..
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 4
Parameterizations for heavy particle
dispersion
P. Astrup
G.T. Csanady
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark
Puff growth

## Slide 5
Experiments used for the investigation
of parameterizations
Wells and Stock (1983), experiments in a horizontal wind tunnel
Wells and Stock dispersion tests: left for 5 micron, right for 57 micron glass spheres.
Vertical velocities 0.1706 m/s respectively 0.545 m/s maintained by an electrical field.
Fall velocities due to gravity: 0.00188 m/s and 0.2316 m/s.
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 6
Snyder and Lumley dispersion tests: left for hollow, right for solid glass beads.
Experiments used for the investigation
of parameterizations
Snyder and Lumley (1971), experiments in a vertical wind tunnel
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 7
Snyder and Lumley dispersion tests: left for corn pollen, right for copper beads.
Experiments used for the investigation
of parameterizations
Snyder and Lumley (1971), experiments in a vertical wind tunnel
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 8
Experiments used for the investigation
of parameterizations
Csanady (1964), outdoor free fall experiments
Concentration variance for airborne particles at 1 m due to parameterization and for
airborne and deposited particles due to particle tracking model. Left 0.1, right 0.2 mm.
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 9
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 10
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 11
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 12
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 13
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 14
Tests of the Csanady parameterization
built into the RIMPUFF dispersion program
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 15
Conclusion
Csanady's dispersion parameterization does reasonably well against the
used wind tunnel dispersion experiments and for Csanady's own outdoor
dispersion experiments.
Building it into the RIMPUFF dispersion program however shows, that if
particles do not have a rather high free fall velocity, the influence on
dispersion is very limited.
When particles get so large and heavy, that dispersion is affected, they fall
to the ground more or less immediately.
If particles are so small and light, that they do not fall to the ground immediately
they disperse like aerosols.
Inclusion of particle falling is thus more important than inclusion of heavy
particle dispersion.
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark

## Slide 16
References
P. Astrup (2016): “Atmospheric dispersion of particles larger and heavier than aerosols”. PREPARE(WP4)-(3)-01.
G.T. Csanady (1963): "Turbulent Diffusion of Heavy Particles in the Atmosphere"
Journal of the Atmospheric Sciences", vol. 21, pp. 201-208, 1963.
G.T. Csanady (1964): "An Atmospheric Dust Fall Experiment"
Journal of the Atmospheric Sciences, vol. 21, pp. 222-225, 1964.
W. H. Snyder and J. L. Lumley (1971): "Some measurements of particle velocity autocorrelation functions in a turbulent flow".
Journal of Fluid Mechanics", vol. 48, part 1, pp. 41-71, 1971.
M.R. Wells and D. E. Stock (1983): "The effects of crossing trajectories on the dispersion of particles in a turbulent flow".
Journal of Fluid Mechanics, vol. 136, pp. 31-62, 1983.
Dispersion and fall out of particles larger and heavier than aerosols
Department of Wind Energy, Technical University of Denmark