## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Fast and simple method with NPP fence measurements for source term estimation and its integration in JRODOS
Juraj Duran, Tatiana Duranova, Jarmila Bohunova (VUJE)
Ivan Kovalets (UCEWP)
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 2: Outline
Basic principles and model application
Input data
Methodology
Uncertainty handling
Outputs
Integration of SIM-S in JRodos

## Slide 3: Basic principles and model application
Algorithm for simple and fast technique for source term estimation (SIM-S) based on simple dispersion model and gamma dose rate measurements in the vicinity of the nuclear facility (VUJE)
Sequential algorithm performs estimation of the released inventory for each 10-min time step using the corresponding meteorological measurements and gamma dose rate measurements in the near vicinity at the fence (distances <800 m from the reactor building)
An old version of module developed in VUJE is applied and working within the National Decision Support System (RTARC, Slovakia)

## Slide 4: Basic principles and model application (cont.)

## Slide 5: Input data
current meteorological measurements from the NPP site (Npp meteostation):
  wind speed [m/s]
  wind direction [deg]
  stability category class [-]
  precipitation intensity [mm/h]
  date [dd.mm.yyyy] of measurement
  time [hh:mm] of measurement
current gamma dose rate measurements in the near vicinity at the fence:
  values of dose rate [Sv/h] from all detectors (averaged for each 10-minutes)
  date [dd.mm.yyyy] of measurement
  time [hh:mm] of measurement

## Slide 6: Input data – teledosimetric system (TDS) example
Measurement points of gamma dose rate for TDS, NPP Temelin (Czech Republic)

## Slide 7: Methodology
The module SIM-S is activated when new data arrived
Based on the analyses of current data and data from the previous time step the module defines:
  how many detectors are affected by release,
  which detectors had been affected for the current time step (detector identification, its coordinates)
  which detectors show error or failure of measurement (too low or zero value or abnormally high value exceeding the detector sensitivity)
Preconditions for the measurements analyses:
  the location of affected detectors should corresponds to the wind direction in the current time step of measurement
  affected detectors should be next to each other
  the measured value of the affected detector should be greater than the background (if the detector was not affected in the previous time step), or greater than the measurement range value of the detector if the detector was affected in some previous time of measurements

## Slide 8: Methodology (cont.)
Estimate of ST for each 10 minutes release
Suppose to have the gamma dose rate data only from maximum 3 or 4 measurement points for each time step
For that reason use the simple method for searching of solution of N linear algebraic equations for N unknown parameters (N measurements, N nuclides activities)

## Slide 9: Database of normalised dose rate
Normalized dose rate (from cloud and deposit exposure) are calculated for different parameters:
  Release height (10 classes of height – maximal height 200 m)
  Initial width (radius) of cloud (10 classes of width – influence of reactor building cavity)
  Category of stability class (6 classes)
  Wind speed (10 classes)
  Intensity of precipitation (10 classes)
Dose rate is calculated for each from 10 representative nuclides

## Slide 10: Database of normalised dose rate (cont.)
Radionuclide MELCORE groups and determined radionuclide representative
Radionuclide group | Radionuclide group representative
1 – Noble Gasses | 133Xe
2 – Alkali Metals | 136Cs
3 – Alkaline Earths | 140Ba
4 – Halogens | 131I
5 – Chalcogens | 132Te
6 – Platinoids | 103Ru
7 – Early Transition Elements | 99Mo
8 - Tetravalents | 143Ce
9 – Trivalents | 140La
10 – More Volatile Main Group | 127Sb

## Slide 11: Database of normalised dose rate (cont.)
Order of calculated released activities of the representative radionuclides for N measurements
N = 1 | 133Xe |  |  |  |  |  |  |  |  | 
N = 2 | 133Xe | 136Cs |  |  |  |  |  |  |  | 
N = 3 | 133Xe | 136Cs | 140Ba |  |  |  |  |  |  | 
N = 4 | 133Xe | 136Cs | 140Ba | 131I |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  | 
N = 10 | 133Xe | 136Cs | 140Ba | 131I | 132Te | 103Ru | 99Mo | 143Ce | 140La | 127Sb

## Slide 12: Uncertainty handling
Methodology takes into account information about uncertainties of dose rate measurements and threshold of measurements (minimal measured value).
As a result we have:
activities for N nuclides (Qi), which give the dose rates closest to real measurements (searching of the minimal square of value the different between measurements and calculate values).
range of activities (ΔQi) which gives the results in the range of uncertainties of dose rate measurements.
Quality of results depends on the number of measurements taken into consideration – the more measurements the less uncertainty of the source term estimate.

## Slide 13: Outputs
  Estimate of released activities of 10 radionuclide representatives from N identified dose rate measurements
  Activity of each radionuclide representative is chosen from the range determined by minimal and maximal value of measured dose rate in current time step
  For the follow-up estimation of source term the best estimate of radionuclide representatives is used
  Activities of other particular radionuclides in each MELCOR group are estimated using the relation of activities of particular nuclides in the defined reactor inventory
The source term determined in such a way represents estimation of the released activity during last 10 minutes, i.e. 10-minutes puff, which is the part of the overall source term. The beginning of the source term estimation is connected with the first exceeding of the measured values over the background and the end is defined by the pre-calculated source term or is given by the system user.

## Slide 14: Integration of SIM-S in JRodos
As it is always done when integrating external models to JRODOS dynamically linked library was created from the original code
Part of code responsible for reading files and initializing input arrays was separated. Instead input data (GDR and meteorological measurements ) are being substituted by requests to database and passing input data to variables of the code
Testing had been performed which assured identity of the results of the original and modified

## Slide 15
Workflow of simple source inversion algorithm within the JRodos system

## Slide 16: User interface of Simple Source Inversion Module

## Slide 17: Results of testing
Artificially generated measurements calculated by JRODOS in detector points
Meteorological scenario: wind speed 2.5 ms, stability D, initial wind direction 260 dec. deg, turning cyclonically on 15 deg. in next 0.5 hour
Source term scenario:

## Slide 18: Calculated gamma dose rate in detector points was used as measurements
Calculated gamma dose rate field with adjusted source term (underestimated by a few times)
Calculated field of gamma dose rate with ‘true’ source term

## Slide 19: Conclusions
Integration of simple source inversion algorithm in RODOS is almost completed
When tested in the JRODOS the method performed reasonably but there was tendency to underestimation of the results
There were also some issues in stability of the algorithm under quickly changed meteorology therefore and for other reasons more testing is required
Exact correspondence between nuclide groups used in simple source inversion method and JRODOS nuclide groups is to be established