## Slide 1
Innovative integrated tools and platforms for radiological
emergency preparedness and post-accident response in Europe
Advanced method for source term estimation and status of its integration in JRODOS
I. Kovalets1, S. Andronopoulos2 , R. Hofman3 and P. Seibert3
1Ukrainian Centre for Environmental and Water Projects
2 National Centre for Scientific Research “Demokritos”
3 Department of Meteorology and Geophysics, University of Vienna
The research leading to these results has received funding from the European Atomic Energy Community Seventh Framework Programme [FP7/2007-2011] [FP7/2012-2013] under grant agreement n° [323287].

## Slide 2: Framework
Collaborative Project “Innovative integrative tools and platforms to be prepared for radiological emergencies and post-accident response in Europe” – PREPARE
Co-funded by EC Grant Agreement n° 323287
Under FP7 THEME: Fission-2012-3.3.1: Update of emergency management and rehabilitation strategies and expertise in Europe

## Slide 3: Basic principles
Advanced technique
“Top-down” / measurement-based / “source inversion” algorithm
Calculate radionuclide emission characteristics:
  Released inventory / isotopic composition of release
  Emission rate and its time-variation
  Release height
Adjust emission characteristics (as modelled) so that results of the atmospheric dispersion model best match the available measurements

## Slide 4: Mathematical formulation
Variational methodology: minimization of a “cost” function
Cost function formulated on differences between:
  model predictions and measurements
  “first-guess” and estimated source term

## Slide 5: Important issues

## Slide 6: Source receptor functions
Source-Receptor Functions – SRF (or sensitivities – SRS) to express model predictions as linear functions of the source term
Dipcot Lagrangian puff dispersion model had been adapted to calculate SRF
In case of stochastic model such as DIPCOT matrix M is stochastic. Proper regularization is achieved by assuming release to be constant withing sufficiently large time subinterval:
Dt_Large
x – ‘reduced’ control vector containing puffs inventories within each time subinterval

## Slide 7: Measurements
Gamma dose rate from monitoring network: relatively fast, dense, frequent; but does not distinguish between nuclides
Activity concentration, ground deposition: nuclide specific; but less dense, not immediately available, poor time resolution
The implemented SRF calculations overall is able to take into account the following measurements:
Gamma dose rate (GDR)
Concentration
Deposition
SRF is calculated for instantaneous measurements and for time integrated measurement as well
The first version of fully integrated within the JRODOS source inversion algorithm deals with GDR and airborne concentration measurements

## Slide 8: First-guess source term

## Slide 9: Uncertainties in first-guess source term
Matrix B – diagonal matrix
Expert judgment: method of calculation – range of uncertainties
“Robust” simplification: magnitude of error equal to certain fraction of norm (maximum value of ) of prior estimation:
For the case of multiple nuclides the above relationship is applied to each nuclide separately.
Default value:
Corresponds to assumption that prior source function is within one order of accuracy

## Slide 10: Observation and model errors
Observation and model errors combined in – diagonal – matrix R
Observation errors: constant, plus a “background” threshold (ɛ)
Fraction αɛ could be >1 in order to reduce weight of measurements which are close to background
Ideally background values are to be present in JRODOS database for each station and each measurement parameter. But since it is presently not the case, constant value ɛ=1e-4 mSv/h is used for gamma dose rate measurements
Default value for gamma dose rate measurements: θo=2e-5 mSv/h
– typical lower sensitivity limit of gamma dose rate measurements
(observation + model errors)

## Slide 11: Model error
Model error:
  Model input parameters assigned on the basis of statistics of model calculations
E.g. typical values of NMSE in atmospheric dispersion modelling in case of exactly known source term is NMSE≈0.5÷10
Default value used: αm=1
From this it could be assumed that

## Slide 12: Multiple nuclide releases

## Slide 13: Ratios of nuclides release rates - examples
Ratios limits used by Saunier et al (2013) in source inversions of Fukushima source term
,
,
Ratios, assessed in this study from the analysis of source terms of VVER1000 reactors
How to take into account such kind of information?

## Slide 14: Dealing with multiple nuclides
To solve this augmentation of cost function and error covariance matrix is used.
Let ratio of release of j-th nuclide (e.g. 137Cs) and 1-st nuclide (e.g.131I) is known approximately

## Slide 15: Dealing with multiple nuclides
The values of rj are calculated from average ratios of emissions of nuclide j to certain nuclide (e.g. nuclide 1) in first guess source term
The values of sigmas of ratios are assumed to be proportional to ratios:
αr≈5 is used for aerosols which correspond to one order of accuracy of initial ratios between releases of aerosols (cf. figures above)

## Slide 16: Release height
Unknown for uncontrolled releases, important for buoyant releases
Method for its inverse estimation:
  Vertically distributed release, Lagrangian puffs emitted at different heights – implemented only in standalone version; not to be implemented within JRODOS due to computational requirements
  Simplification implemented for JRODOS version: source inversion problem is solved separately for several supposed source heights. The source height at which the best value of cost function was achieved is chosen as solution

## Slide 17: Implementation details
Minimization problem solved with NNLS (Non-Negative Least Squares) method as implemented in freeware NETLIB library (www.netlib.org). The method is extracted from library and integrated into the DIPCOT-source inversion code
Run of source inversion method within JRODOS is basically similar to LSMC run. It can use the same source term information input via RoLite (in this case source terms are considered as prior estimations), the same kinds of weather information (NWP or hand input) is used.
The one important differences is that concentration fields are not calculated on grid but only in points of observations – for optimization purposes
The output result – estimated source function could be exported to xml file and used in ‘normal’ LSMC run
Source receptor functions are also available to user who can wish to ‘play’ with source term estimation outside JRODOS

## Slide 18: Test case: description
Geographical domain – meteorology – topology of sensors – source location: ETEX European Tracer Experiment
Hypothetical release of 21 nuclides, 2 release phases of 0.5 and 4 h, separated by 2h of no release (source term Muehleberg-1 from flexRISK, http://flexrisk.boku.ac.at/)
Release rates from 0 to 1012 Bq/s
Vertically distributed release, described by 10 vertical levels with Gaussian profile (0–100m, mode at 50m)

## Slide 19: Test case: description

## Slide 20: Test case: modelling
Synthetic measurements produced by running Lagrangian puff dispersion model DIPCOT with “true” source term:
  10-min gamma dose rate “measurements” from 59 stations
4 time-phases for the description of the release: 2h before 1st release, 1st release, 2nd release, 2h after 2nd release
SRFs have been calculated by DIPCOT and exported to module solving inverse problem
  Time step of 0.5 h
Ratios of nuclide release rates enter the mathematical problem as additional linear equations; corresponding error variances allow controlling enforcement of prescribed values

## Slide 21: Test case: solution experiments
Influence of time resolution used for the description of the release
  1st experiment: release rate of each nuclide constant in each of the 4 phases
  2nd experiment: release rate of each nuclide varies in each of the 4 phases with a time step of 0.5 h

## Slide 22: Testing of Source-Receptor Matrix
Chart: time, s
Run | normr | norm0 | normr/norm0
0 | 2.81E-06 | 0.3629 | 7.75E-06
1 | 0.012 | 0.3629 | 3.31E-02
Comparison of gamma dose rate at sensor No. 59 calculated in forward run and calculated with source-receptor matrix
Norms of residual ||r=Gx-b|| as compared to norm of measurement vector ||b||.
Run0 – the same run in which source-receptor matrix G was calculated; Run 1 – independent run

## Slide 23: Results - specified sigmas
1st experiment
results are acceptable and resolve the most important features of the release (timing and magnitude of higher emissions)
Differences in lower emissions are due to differences in emission in different vertical sources even in one phase

## Slide 24: Results - specified sigmas
1st experiment: vertical profiles for emissions of selected nuclides in different phases

## Slide 25: Results - specified sigmas
2nd experiment: more elements in source matrix
Timing of releases was estimated correctly — periods with no releases were more or less preserved
Better agreement for higher releases

## Slide 26: Results – automatically calculated; default parameters
Chart: Kr-87
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 0 | 0 | 0 | 0 | 350578100000 | 0 | 0 | 0 | 586657800 | 1133845000 | 873175200 | 823289500 | 523898000 | 135776600 | 2545807000 | 0 | 0
 | 0 | 0 | 0 | 0 | 532825500000 | 0 | 0 | 0 | 10870420000 | 1384710000 | 203019200 | 213076400 | 314329500 | 0 | 432304100 | 0 | 0
Chart: Cs-137
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 0 | 0 | 0 | 0 | 31606780000 | 1985370000 | 620672100 | 0 | 0 | 452190800 | 461278800 | 422056200 | 400223600 | 7175298 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 19724880000 | 0 | 0 | 3478608000 | 1101072000 | 0 | 0 | 232600700 | 127133600 | 0 | 0 | 0 | 0
Chart: I-131
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 4704750 | 6298444 | 4607272 | 6481344 | 67361000000 | 29042740000 | 23072990000 | 13961450000 | 5139119000 | 4848882000 | 4269017000 | 2490984000 | 1471094000 | 293468100 | 95831110 | 0 | 0
 | 0 | 0 | 0 | 0 | 197751200000 | 0 | 4985342000 | 1178096000 | 0 | 3629123000 | 3164752000 | 3509152000 | 2738322000 | 0 | 0 | 0 | 0
First guess source function is shifted in time 2 hrs before true source rate and multiplied by 10
Dots – true source function
Line – analyzed source function

## Slide 27: Results – automatically calculated; default parameters
Chart: Kr-87
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 0 | 0 | 0 | 0 | 350578100000 | 0 | 0 | 0 | 586657800 | 1133845000 | 873175200 | 823289500 | 523898000 | 135776600 | 2545807000 | 0 | 0
 | 0 | 0 | 0 | 0 | 24299200000 | 0 | 0 | 0 | 7940614 | 867733700 | 645451200 | 941117500 | 729162800 | 158704300 | 3384061000 | 0 | 0
Chart: Cs-137
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 0 | 0 | 0 | 0 | 31606780000 | 1985370000 | 620672100 | 0 | 0 | 452190800 | 461278800 | 422056200 | 400223600 | 7175298 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 14167370000 | 6022981000 | 211758700 | 0 | 0 | 0 | 0 | 0 | 16326240 | 7963630 | 0 | 0 | 0
Chart: I-131
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 4704750 | 6298444 | 4607272 | 6481344 | 67361000000 | 29042740000 | 23072990000 | 13961450000 | 5139119000 | 4848882000 | 4269017000 | 2490984000 | 1471094000 | 293468100 | 95831110 | 0 | 0
 | 0 | 5786482 | 4466810 | 6034264 | 54590870000 | 37427390000 | 29001210000 | 17029240000 | 7587473000 | 8628923000 | 4833588000 | 2478485000 | 1477103000 | 477807800 | 23558090 | 0 | 0
First guess source function is shifted in time 2 hrs before true source rate and multiplied by 0.1
Dots – true source function
Line – analyzed source function

## Slide 28: Conclusions
An advanced method for source term estimation based on measurements and Lagrangian puff atmospheric dispersion model is developed and tested.
The main difficulty in application of the method is in specification of set of empirical parameters – root mean square errors of prior source function, observations, model and nuclide ratios
The first test results obtained for realistic emission scenarios with multiple nuclides, distributed releases and pre-specified (adjusted) parameters values were very encouraging
The results obtained in automatic mode of method application with defaults values of parameters were reasonable as well
The method is currently being integrated in JRODOS. Currently the method could run within the JRODOS and produce results. Most of the input parameters are already initialized through JRODOS user interface and databases (weather, source term). But still some of the parameters (measured values, steering parameters and output results) are yet read/written through files.
The final integration is expected within 1 month