## Slide 1
CONFIDENCE WP1
Overview
Irène Korsakissok, IRSN
Notes: Good morning, I’m (Irène Korsakissok, leader of WP1). I’m pleased to be here and have the privilege of introducing the 1st block of presentations of this workshop. I am going to give a you brief overview of WP1’s achievements during these 3 years.

## Slide 2
Country (8) | Participant (13) | Contact
France | IRSN | Irène Korsakissok (lead) Karine Chevalier Jabet Damien Didier Anne Mathieu
 |  | Raphaël Périllat (PHIMECA)
Germany | KIT | Wolfgang Raskob
 | BfS | Florian Gering Thomas Hamburger
Greece | EEAE | Spyros Andronopoulos
Norway | NMBU | Deborah Oughton
 | NMI-MET | Heiko Klein Erik Berge Magnus Ulimoen
 | NSA | Jan Erik Dyve
UK | PHE | Stephanie Haywood
 |  | Peter Bedwell Joseph Wellings
 | UK MET | Susan Leadbetter
 |  | Andrew Jones
Denmark | DTU | Andrey Sogachev Poul Astrup
Netherlands | RIVM | Chris Twenhöfel
 |  | Jasper Tomas
 | KNMI | Gertie Geertsema
 |  | Hans de Vries
Hungary | MTA EK | Csilla Rudas Péter Szántó Tamás Pázmándi
The CONFIDENCE project
7 work packages (WPs)
WP1: uncertainties in the pre and early release phase
  WP1 members
High uncertainties: lack of / partial information on facility events, forecast errors…
Use of atmospheric dispersion simulations (no observations available)
Input for other WPs (with the limit of timing between different tasks)
Notes: In the CONFIDENCE project, WP1 is devoted to uncertainties in the pre and early release phase. It included 13 participants from 8 European countries.
A particularity of this phase is that we are dealing with high uncertainties, related to partial information on facility events and forecasts errors, as we are trying to anticipate the consequences of events that have not occurred yet. It follows that we are heavily relying on atmospheric dispersion simulations, as no observations are available yet.
As WP1, we were also providing input for the other WPs dealing with later phases of the accident.

## Slide 3
WP1: tasks
2017
2018/2019
2019
1.1 Analyzing and ranking sources of uncertainties
  Using ensemble data for meteorological uncertainties (Lead: S. Leadbetter, MetOffice)
  Using meteorological measurements to reduce uncertainties (Lead: S. Andronopoulos, EEAE)
  Uncertainties related to source term (Lead: A Mathieu, IRSN)
  Uncertainties related to models (Lead: P. Bedwell and J. Wellings, PHE)
1.2 Uncertainty propagation and analysis
  Hypothetical accident scenarios in Europe: the REM case (Lead: I. Korsakissok, IRSN)
  Hypothetical accident scenarios in Europe: the Western Norway case (Lead: Heiko Klein and Erik Berge, NMI MET)
  Comparisons to observations and indicators to assess the quality of an ensemble: the Fukushima case (Lead: I. Korsakissok, IRSN)
1.3 Emergency response and dose assessment
  Food chain uncertainty propagation (Lead: T. Hamburger, BfS)
  Recommendations and operational methodology in an emergency context (Lead: P. Bedwell, PHE)
Notes: WP1’s (work?) was divided into 3 tasks. The first one was devoted to analyze and rank the sources of uncertainties, and was carried out during the first year of the project.
Among the prime sources of uncertainties are the weather forecasts (which we all know are uncertain!) and the assessment of the source term, that is, what is thought to be released in the atmosphere by the damaged installation. Finally, we are using models which are also subject to errors coming from numerical and physical approximations.
Once these uncertainties have been described and quantified, they have to be propagated through ADMs, in order to (infer) see how they influence the output results (such as dose calculations). This was done during the 2nd and 3rd years of the project, on hypothetical accident scenarios in Europe and on the Fukushima accident.
The 3rd task was related to food chain uncertainty propagation, and recommendations for the use of ensemble calculations in an emergency response context.

## Slide 4: WP1: deliverables
Task | Deliverable | Lead | Date
Task 1.1 | Analyzing and ranking sources of uncertainties |  | 
 | D1.1 Guidelines ranking uncertainties for atmospheric dispersion | IRSN (with subtask leaders) | M12 (24/12/2017)
 | D1.2 Published dataset of meteorological ensemble data | UK Met Office | M06 (23/06/2017)
Task 1.2 | Uncertainty propagation and analysis |  | 
 | D1.3 Published set of probability maps of threshold exceedance for scenarios provided to WP4-6 | IRSN | M06 (23/06/2017) & M24 (24/12/2018)
 | D1.4 Guidelines for the use of ensemble calculations in an operational context, indicators to assess the quality of uncertainty modeling and ensemble calculations, and tools for ensemble calculation in emergency response | IRSN (with subtask leaders) | M34 (24/10/2019)
Task 1.3 | Emergency response and dose assessment |  | 
 | D1.5 Software tool which allows the propagation of uncertainties up to the dose assessment models | BfS | M34 (24/10/2019)
Notes: Corresponding to the 3 tasks, were 5 different deliverables. I will talk about some of them later, but now, let me go back to task 1.1.

## Slide 5: Ensembles Workshop – Paris, June 2017
  How well do ensembles represent the uncertainty in the meteorology?
  Do ensembles represent the uncertainty in variables of interest for dispersion models?
  Are additional meteorological perturbations necessary for dispersion modelling?
Atmospheric state at present time
Atmospheric state at future time
True state
Ensemble members
Presentations from and discussions between WP1 members, Météo France, Hungarian Met Service and DMI covering:
Task 1.1.1: Using Ensemble Meteorological Forecasts to Represent Meteorological Uncertainty in Dispersion Models
Notes: As I said, one of the major sources of uncertainties are meteorological forecasts; fortunately, weather offices have developed methods to take into account the uncertainties: they rely on meteorological ensembles, that is, an ensemble of « possible future states of the atmosphere » (instead of a single one), that result in a probabilistic forecast.
Early in the project, we organised a workshop bringing together WP1 members and specialists of weather forecast, to discuss issues such as…

## Slide 6: Task 1.1 Further on input uncertainties…
http://www.concert-h2020.eu/en/Publications
Notes: To go further on the topic as well as ST and model uncertainties, I refer you to deliverable D9.1 « guidelines… » which consists in 5 separate reports with different lead authors, each report describing a particular source of uncertainties and how to take them into account.

## Slide 7: Task 1.2 – uncertainty propagation and analysis
  Definition of meteorological scenario:
    Select a date (rain or not, high or low variability…)
    Choice of meteorological model, domain, spatial and temporal resolution
    ensemble of N meteorological members (representative of the uncertainty)
  Hypothetical accident scenarios in Europe: the REM case (Lead: IRSN)
  Hypothetical accident scenarios in Europe: the Western Norway case (Lead: NMI MET)
  Comparisons to observations and indicators to assess the quality of an ensemble: the Fukushima case (Lead: IRSN)
  Definition of release scenario and associated uncertainties:
    Release time
    Isotopic composition
    Released quantity as a function of time and radionuclide
    Release height
Participants to the case study use their own atmospheric dispersion model and propagate the uncertainties, resulting in an ensemble of outputs (dose, deposition…)
Case study leader collect the results and carry out the ensemble inter-comparison
Notes: Now, the following task consisted in taking these input uncertainties and propagating them through ADMs. This was done for different case studies. Each time, a « scenario » consisted in defining a meteorological scenario (i.e. a date with / without rain, high or low variability in wind direction…) and a release scenario (i.e. release time, quantity, composition, and associated uncertainties). Then, participants to the case study used their own ADMs to propagate these uncertainties. The task leader then collected and analysed the results.
It is like an inter-comparison exercise, except that instead of each participant having one single output, they each had several tens or hundreds of simulations!

## Slide 8
Case studies |  |  |  | Fukushima | REM (Borssele) |  |  | Western Norway
 |  |  |  |  | REM1-S | REM2-S | REM-L | 
Source term |  |  |  | 9 ST from the literature | Short release: 4 hours Variation in height, release time and quantity |  | Long release: 72 hours 10 ST | Explosion and fire– variation in height and particle size
Meteorological ensemble |  |  |  | ECMWF-ENS 0,2° Provided by Met Office Time resolution: 1h Forecast length: 72h Members: 51 | Harmonie hybrid lagged ens 2,5 km Provided by KNMI Time resolution: 1 hour Forecast length: 72 hours Members: 10 |  |  | Harmonie 2,5 km Provided by NMI MET Time resolution: 1h Forecast length: 72h Members: 10
Release date |  |  |  | 14-16 March 2011 | 11 Jan. 2017 easy case | 12 Jan. 2017 storm front | 11-13 Jan. 2017 | 16 March 2017
Participant |  | Model | Type |  |  |  |  | 
France | IRSN | ldX | Eulerian | X | X | X | X | 
Germany | BfS | RIMPUFF | Gaussian puff |  | X | X | X | 
EEAE | EEAE | DIPCOT | Lagrangian puff | X | X | X | X | X
Norway | NMI MET | SNAP | Lagrangian particle | X |  |  |  | X
UK | MET OFFICE / PHE | NAME | Lagrangian particle | X | X | X | X | 
Denmark | DTU | RIMPUFF | Gaussian puff | X | X | X | X | 
Netherlands | RIVM | NPK-PUFF | Gaussian puff | X | X | X | X | 
Hungary | MTA EK | SINAC | Gaussian puff |  | X | X |  | 
Number of participants |  |  |  | 6 | 7 | 7 | 6 | 2
Notes: Here is a synthesis of all the case studies carried out during the project. Apart from Fukushima, there were 2 different case studies, and one of them, the REM case study, consisted itself in 3 different scenarios. Each case study had several participants and different meteorological and release characteristics.

## Slide 9: Tasks 1.2 and 1.3
Presentations from and discussions between WP1 members, WP5-WP6 representatives, covering
Workshop on ensemble analysis and visualisation – Munich, February 2019
  Uncertainty propagation: how to construct a good ensemble?
  What are the uncertainties not taken into account?
  How to analyze and compare ensemble results?
  What variables and indicators should be recommended?
  How to visualize uncertainties?
Notes: To analyse this huge amount of data, we organized another workshop, this time on ensemble analysis and visualisation, which brought together people from WP1, 5 and 6….
In the following presentations, you will see a panel of different ways of visualizing uncertainties.

## Slide 10: Tasks 1.2 and 1.3 Uncertainty propagation results and operational guidelines
http://www.concert-h2020.eu/en/Publications
Notes: Again, I refer you to deliverable D9.5 which summarizes all the results of the case studies, as well as the food chain propagation and operational recommendations from task 1.3.

## Slide 11: Dissemination
NKS seminar on ensemble dispersion, Copenhagen (Denmark), September 2018: invited presentation
19th NERIS workshop, Roskilde (Denmark), April 2019
19th HARMO conference, Bruges (Belgium), June 2019
  special session on ensembles organized by CONFIDENCE WP1
  9 presentations, including 6 from CONFIDENCE WP1 members
  Conference proceedings
Workshop on ensemble dispersion organized by MeteoSwiss, Zurich (Swiss), August 2019: invited presentation
Radioprotection special issue
CONFIDENCE dissemination workshop: following…
  Presentations of meteorological and source term uncertainties (task 1.1)
  Presentations of results from the 3 case studies (task 1.2)
  Synthesis of operational recommendations (task 1.3)
  Further information on posters!
Notes: …