## Slide 1
CONFIDENCE WP1
Source Term Uncertainties
Jasper Tomas
National Institute for Public Health and the Environment (RIVM), The Netherlands

## Slide 2: Source term uncertainties
Accident scenario
Reactor status
Source term
  Timing
  Released quantities
  Isotopic composition
  Effective release height
  Chemical form of isotopes
  Physical form of isotopes: particle size distribution
D9.1 – Guidelines ranking uncertainties for atmospheric dispersion
Notes: In general, source term uncertainties arise from uncertainties in the accident scenario, the subsequent status of the reactor to possible release scenarios resulting in the source term.

## Slide 3: Accident scenario: timeline with uncertainty
Assessment (exceedance of Intervention Levels?)
Meteorological data required
Release
Release duration
Prognosis duration
Now
Reactor
shutdown
Delay (containment)
Time to release
Time
Notes: Introducing uncertainty in the “Time to release” can make the timeline quite complex. This schematic presentation can help.

## Slide 4: Radiological Ensemble Modelling (REM) study
Location

## Slide 5: Radiological Ensemble Modelling (REM) study
Two hypothetical source terms:
 | ‘Short release’ | ‘Long release’
Based on | Standard source term in the Netherlands scaled to a 900 MWe reactor | FASTNET ensemble, Loss of Coolant Accident
Time to release | 24 h +/- 6 h, equally distributed | 0 hours, no uncertainties
Release duration | 4 hours | 3 days
Effective release height | 50 m +/- 50 m, equally distributed | 50 m +/- 50 m, equally distributed
Released activity | Factor 1/3 to 3 of the reference source term (~1% of Iodine in inventory) | Given by the spread of the ensemble of source terms
Notes: To hypothetical source terms were defined: a short release (4 hours) with a high uncertainty in the release time, and a longer release (3 days) that has low uncertainty in the release time as it takes place ‘ now’.

## Slide 6: To remember:
For the discussions:
‘Short release’: Generic 4 hour release, high uncertainty in release time
‘Long release’: based on FASTNET ensemble, ‘Loss of Coolant Accident’ (LOCA), 72 hour release, takes place ‘now’.
Reading material about source term uncertainty and their effects:
Deliverable 9.1.3 “Guidelines describing source term uncertainties”
Poster: “Design of an ensemble of source terms representative of uncertainties in case of a severe nuclear accident”, Chevalier-Jabet et al.
..and of course: D72/D/9.5 – “WP 9.3 Guidelines for the use of ensemble calculations in an operational context, indicators to assess the quality of uncertainty modelling and ensemble calculations, and tools for ensemble calculation in emergency response”

## Slide 7
Thank you