## Slide 1
CONFIDENCE WP1
Ensemble calculations for the atmospheric dispersion of radionuclides. Hypothetical accident scenarios in Europe: the REM case studies
Hans De Vries, Gertie Geertsema, Irène Korsakissok, Susan Leadbetter, Raphaël Périllat, Rinus Scheele, Jasper Tomas
Based on calculations from: Spyros Andronopoulos, Poul Astrup, Peter Bedwell, Tom Charnock, Thomas Hamburger, Ievgen Ievdin, Susan Leadbetter, Tamás Pázmándi, Raphaël Périllat, Csilla Rudas, Andrey Sogachev, Péter Szántó, Joseph Wellings

## Slide 2: Uncertainty propagation: the Radiological Ensemble Modelling (REM) case study
Hypothetical accident in Europe
Propagation through Atmospheric Dispersion Models (ADMs)
Seven participants with different models
Questions
Are uncertainty assessments very different from one participant to another?
How does the inter-participant variability compare with the propagated uncertainties?
Impact of meteorological vs source term uncertainties?
What variables / indicators / thresholds are relevant to represent output uncertainties?
inter-comparison of ensemble results

## Slide 3: The REM case studies –scenarios
REM1: “small variability”
  Release at 12 UTC on January 11, 2017
  established wind direction
  patchy rain
REM2: “warm front passage”
  Release at 21 UTC on January 12, 2017
  Wind direction turning
  High rain episodes
Long release scenario: See poster (Chevalier Jabet et al)
REM-1 scenario: See HARMO 19th presentation and proceedings
See deliverable D9.5.2 (Korsakissok et al) for more results
2 source term scenarios
2 meteorological scenarios
Short release scenario
  Duration 4 hours
  Uncertainties in the pre-release phase
Long release scenario
  Duration 72 hours
  Uncertainties in the release phase
          Release time +/- 6 hours
          Release height 50m +/- 50m
          Released quantity x [1/3, 3]

## Slide 4: REM2 case study – short release
Country | Participant | Type of model | Number of simulations | Meteorological perturbations | Source perturbations |  | 
 |  |  |  |  | Release height | Release time | Released quantity
France | IRSN | ldX – Eulerian | 150 (450) | 10 members | [0m, 50m, 100m] | T0 + [-6h, -3h, 0h, +3h, +6h] | [x1/3, x1, x3]*
Germany | BfS | RIMPUFF – Gaussian puff | 150 (450) | 10 members | [0m, 50m, 100m] | T0 + [-6h, -3h, 0h, +3h, +6h] | [x1/3, x1, x3] *
UK | MetOffice/ PHE | NAME – Lagrangian particle | 90 | 10 members | [50m] | T0 + [-6h, 0h, +6h] | [x1/3, x1, x3]
Greece | EEAE | DIPCOT – Lagrangian puff | 50 (150) | 10 members | [50m] | T0 + [-6h, -3h, 0h, +3h, +6h] | [x1/3, x1, x3] *
Hungary | MTA EK | SINAC – Gaussian puff | 90 (270) | 10 members | [0m, 50m, 100m] | T0 + [-6h, 0h, +6h] | [x1/3, x1, x3] *
The Netherlands | RIVM | NPK-puff – Gaussian puff | 650 (1950) | 10 members | [0m, 25m, 50m, 75m, 100m] | [-6h, +6h] with a time step of 1 hour (13 steps) | [x1/3, x1, x3] *
Denmark | DTU | RIMPUFF – Gaussian puff | 50 (150) | 10 members | [50m] | T0 + [-6h, -3h, 0h, +3h, +6h] | [x1/3, x1, x3] *
*Perturbation applied a posteriori on the results
7 participants
Different (types of) models: 1 Eulerian, 2 Lagrangian, 4 Gaussian puffs
Different number of members in the ensembles: from 90 to 1950!

## Slide 5
Enpoints and ensemble outputs
Deterministic: one simulation
137Cs deposition, threshold 37 kBq/m2
Maximum
distance D above threshold
Probabilistic: 137Cs ground deposition for N simulations
N maps of deposition: “postage stamp”
Median (or 25th, 75th percentile…) of the N deposition maps
For a given threshold t
N maximum distances Di above t
Map of probability of exceeding t
Mean 361 km
Range 16–586 km
Endpoints: consequences computed at T0+24h
  Ground deposition of 137Cs : Post-Chernobyl reference level 37 kBq/m2 for 137Cs
  Effective dose and inhalation thyroid dose for 1-year old child – 10, 50, 100 mSv
How to use ensemble results?

## Slide 6
Different meteorological fields
T0 = 15:00 UTC
T0 = 03:00 UTC Day+1
T0 = 21:00 UTC
  137Cs deposition (kBq/m2)
  at T0+24h – IRSN
REM2: “postage stamp”

## Slide 7
DTU
IRSN
MetOffice
BfS
RIVM
MTA EK
Differences may come from:
Type of models
Different wet deposition schemes
Diffusion coefficients
Modelling domain, interpolation…
EEAE
RIMPUFF – Gaussian puff
RIMPUFF – Gaussian puff
DIPCOT– Lagrangian puff
NAME – Lagrangian
LdX– Eulerian
NPK-puff – Gaussian puff
SINAC – Gaussian puff
REM2: “median” (percentile 50)
  137Cs deposition (kBq/m2)
  at T0+24h – 7 participants
10 simulations (meteorology only)

## Slide 8
Maps of probability of threshold exceedance
For a threshold of 37 kBq/m² for the 137Cs deposition
10 simulations (meteorology only)
90 simulations (meteorology + source term)
Mean 268 km
Range 211–433 km
Mean 192 km
Range 25–525 km
With source perturbations
Maximum distance of threshold exceedance is lower
Surface covered by low probabilities is larger
REM2: “frequency maps”
  137Cs deposition (kBq/m2)
  at T0+24h – UK MetOffice
See REM2 poster!

## Slide 9
BfS
N=450
RIMPUFF – Gaussian puff
DTU
N=150
RIMPUFF – Gaussian puff
EEAE
N=150
DIPCOT– Lagrangian puff
MetOffice
N=90
NAME – Lagrangian
IRSN
N=450
LdX– Eulerian
RIVM
N=1950
NPK-puff – Gaussian puff
MTA EK
N=270
SINAC – Gaussian puff
REM2: “frequency maps”
  137Cs deposition (kBq/m2)
  at T0+24h – 7 participants
For a threshold of 37 kBq/m² for the 137Cs deposition
Some ensembles feature an area of (low probability) threshold exceedance in the North-Eastern area (others are below 5%)
Corresponds to the change in wind direction

## Slide 10
Maximum distance from the source (km)
For a threshold of 37 kBq/m² for the 137Cs deposition
10 simulations (meteorology only)
30-1950 simulations (meteorology + source term)
Larger variability (boxes’ size) with ST perturbations
Inter-model variability not totally encompassed by the range of variation
REM2: “box plots”
  137Cs deposition (kBq/m2)
  at T0+24h – 7 participants

## Slide 11
Maximum distance from the source (km)
Thresholds on the effective and inhalation thyroid doses
10 mSv - Effective dose
50 mSv - Inhalation thyroid dose
Good agreement between the uncertainty estimations and median values
A few outliers in some ensembles give much larger distances
REM2: “box plots”
  Effective and thyroid inhalation doses (mSv) at T0+24h – 7 participants

## Slide 12: Conclusions
Influence of source perturbations
    Importance of taking into account source perturbations (especially release time!)
    Larger ensembles’ spread
    More perturbations may induce lower distance above a given threshold
Inter-model variability
    Less important when overall uncertainties are larger
    Some models or configurations may be more appropriate to the case
    Part of this variability may be taken into account
    An uncertainty assessment with only one model will always be partial
Uncertainty assessment
    Lower threshold induces higher distances / probability
    Surface above threshold (instead of distance) limits the effect of outliers
    Importance of choosing correctly the threshold and percentile