## Slide 1
CONFIDENCE WP1
The Fukushima case study: ensemble results and indicators to assess the quality of ensembles
Irène Korsakissok, Raphaël Périllat
Spyros Andronopoulos, Poul Astrup, Peter Bedwell, Erik Berge, Arnaud Quérel, Heiko Klein, Susan Leadbetter, Olivier Saunier, Andrey Sogachev, Jasper Tomas, Magnus Ulimoen

## Slide 2
Questions
Do the ensembles reproduce output variability (i.e. encompass observations)?
Are there lacks in the uncertainties taken into account (i.e. observations not well reproduced, under-dispersed ensembles)?
How do ensembles’ performance vary from one participant to another? Can we discriminate between the different models/approaches?
What variables /indicators to assess the quality of ensembles by comparison to observations?
Uncertainty propagation: the Fukushima accident
Propagation through Atmospheric Dispersion Models (ADMs)
Six participants with different models: inter-comparison of ensemble results
Numerous environmental observations: a unique case for ensemble evaluation
Key objective:
to assess the quality of uncertainty modelling

## Slide 3: The Fukushima accident
3 weeks of accident with major releases, from March 11th 2011
Multiple episodes with several reactors involved
Complex terrain (coastal area, valleys, mountains)
Complex meteorology (stable situations, low wind speed / changing wind direction during crucial release episodes, rain/snow, fog…)
Meteorological models still show difficulties to reproduce the complex fields
No deterministic combination of meteorology / source term / ADM is able to reproduce different observations for all times
9 years later, meteorological and ST uncertainties are still high

## Slide 4: Uncertainty propagation for the Fukushima case
131I
137Cs
Focus on 3 days: 14-16 March 2011
  Major releases, most important contamination over Japan land
  Stable situation, turning winds, wet deposition
Source term scenario
All ST available in the literature reconstructed with the help of environmental observations (a posteriori)
9 source terms from the literature with various release kinetics
Total released quantity over the 3 days:
137Cs factor 7 (3.1-21.4 PBq) between the different ST
131I factor 9 (46-400 PBq) between the different ST
Meteorological scenario
ECMWF ensemble
0,2° horizontal resolution
36 vertical levels
1-hour time resolution
51 members

## Slide 5: Uncertainty propagation for the Fukushima case
Participant |  | Type of model | Number of simulations (perturbations)
France | IRSN | ldX – Eulerian | 200 simulations (MC)
The Netherlands | RIVM | NPK-puff – Gaussian puff | 459 simulations (9 ST x 51 MET)
UK | Met Office (MO) | NAME – Lagrangian particle | 102 simulations (2 ST drawn randomly among 9 x 51 MET)
Greece | EEAE | DIPCOT – Lagrangian puff | 459 simulations (9 ST x 51 MET)
Denmark | DTU | RIMPUFF – Gaussian puff | 459 simulations (9 ST x 51 MET)
Norway | NMI MET | SNAP – Lagrangian particle | 459 simulations (9 ST x 51 MET)
6 participants
Different (types of) models: 1 Eulerian, 3 Lagrangian, 2 Gaussian puffs
IRSN used Monte Carlo scheme and added perturbations on physical model parameters (wet/dry deposition, diffusion…)
Different number of members in the ensembles: from 200 to 459

## Slide 6: Comparison with radiological observations
Integrated over all radionuclides
Plume shine + ground shine
Temporal resolution (1-hour)
Cs-137 only - over 3-weeks release periods
Spatial resolution (< 1km)
3 kinds of observation data
Gamma dose rate
137Cs air concentration
137Cs deposition
Cs-137 only – air activity near ground
Temporal resolution (1-hour)

## Slide 7: Comparison with observations Fukushima city
137Cs air concentrations (Bq/m3)
MO
RIVM
IRSN
DTU
EEAE
NMI
All ensembles globally encompass the observations
Observations not within some ensembles are very low (< 1 Bq/m3)
The 25-75th percentiles of the ensembles (dark blue) show variations
Large variations in the maximum values obtained by different participants: from 103 to 104 Bq/m3
The maximum value of the observations at this station is 33 Bq/m3: some members of the ensembles hugely overestimate the concentrations
Red: observations
Blue: ensemble members
Dark blue: 25-75th percentiles

## Slide 8: Comparison with observations Fukushima city
Gamma dose rates (nSv/h)
MO
RIVM
IRSN
DTU
EEAE
NMI
All ensembles encompass the observations
Not the case for all 25-75th percentiles of the ensembles (dark blue)
Beginning of wet deposition is correctly forecast by (some members of) the ensembles
Rainfall rate (mm/h)
Black: observations
Blue: ensemble members
Dark blue: 25-75th percentiles
Grey: meteorological members
Red: rain gauge observations
Background radiation
Abrupt increase of dose rate due to wet scavenging
Dose rate after plume passage is high (wet deposition)

## Slide 9: Comparison with observations Iwaki
Gamma dose rates (nSv/h)
MO
RIVM
IRSN
DTU
EEAE
NMI
All ensembles encompass the observations
Not the case for all 25-75th percentiles of the ensembles (dark blue)
Ensemble members forecast rain on March 14th during 1st plume passage, resulting in wet deposition, which is incorrect
Rainfall rate (mm/h)
Black: observations
Blue: ensemble members
Dark blue: 25-75th percentiles
Grey: meteorological members
Red: rain gauge observations
Successive peaks of dose rate indicating plume passages
Dose rate after plume passage is low (low deposition)

## Slide 10: Comparison with observations Indicators to assess the quality of an ensemble
Rank histograms
Represent the ability of an ensemble to encompass the observations
The rank of each member corresponds to the number of observations below it
If the ensemble was “perfect”, the rank diagram would be flat
Ensemble under-dispersive: U-shaped, over-dispersive: ∩-shaped
High bar on one side: bias
Gamma dose rates (nSv/h)
137Cs air concentrations (Bq/m3)
Rank diagrams for Met Office
See Fukushima poster!

## Slide 11: Conclusions
Fukushima provided a unique case study to compare ensemble simulations with radiological observations
In this case, source term and meteorological uncertainties are much larger than inter-ensemble variability
All ensembles show a similar performance to encompass the observations;
  acceptable for air concentrations
  good for gamma dose rates
There is a large variability between participants when looking at the median or 25th-75th percentiles
Most ensembles feature very large overestimation of the concentrations (by a decade or two) for some members
  Is the uncertainty estimation too large?
  Raises the issue of how to use ensemble simulations in an operational context (maximum values vs chosen percentile…)