## Slide 1
CONFIDENCE WP1
Hypothetical accident scenarios in Europe: the Western Norway case study
Erik Berge, Heiko Klein
Magnus Ulimoen, Spyros Andronopoulos, Ole Christian Lind, Brit Salbu, Naeem Syed

## Slide 2: Background
Increased Russian and allied activity of nuclear vessels in the Norwegian and the North Seas.
The number of allied nuclear submarines in Norwegian ports has increased from 10-15 to 30-40 per year during the last 5-10 years.
Uncertainty analyses:
  10 meteorological ensembles form a high resolution (2.5 km ) model.
  5 emission scenarios describing a fire in a nuclear vessel
  Two preparedness dispersion models – SNAP of Norway – DIPCOT of Greece.
Oslo
Bergen
L
16.03.2017 21 UTC
EPS member 0, 2.5 km
By Elena Dider - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=81925985
Akademik Lomonosov

## Slide 3: Meteorological uncertainty
Vikedal
Source
At Vikedal
At source
Wind direction
Wind speed
3 h precipitation
Solid line: 50th percentile: Dark blue: 10th to 90th percentile
Probability of more than 20 mm in 24 h
Stavanger
Haugesund

## Slide 4: Emission scenarios
First hour
Emissions for 7 hours starting 09 UTC and ending 16 UTC 16.03.2017.
5 emission scenarios
Log-normal particle size distribution
Same total release of 5.41·1017 Bq for all 5 scenarios
First hour: Instant mixing up to 500 m
After first hour: Instant mixing up to 200 m
Fraction of total release (%) during each of the 7 hours.
Scenario 1: Constant release
Scenario 2: 25 % first hour
Scenario 3 (reference): 50 % release first hour
Scenario 4: 75 % first hour
Scenario 5: 90 % first hour

## Slide 5: Dispersion models
Participant |  | Type of model | Number of simulations (perturbations)
Greece | EEAE | DIPCOT – Lagrangian puff | 50 simulations (5 ST x 10MET)
Norway | MET (NMI) | SNAP – Lagrangian particle | 50 simulations (5 ST x 10 MET)
SNAP 137Cs (Bq/m3) at 30 m height level
DIPCOT 137Cs (Bq/m3) at 1 m height level
Simulation for one day (10 UTC 16.03.2019 to 09 UTC 17.03.2019)
EPS member 0 and emissions scenario 3 (50 %)

## Slide 6: Accumulated concentrations and depositions during 24 hours
Accumulated concentrations (10 EPS and 5 emission scenarios)
10th percentile
50th percentile
90th percentile
SNAP
DIPCOT
10th percentile
50th percentile
90th percentile
Accumulated depositions (10 EPS and 5 emission scenarios)

## Slide 7: Summary
The spread (uncertainty) in the calculated radioactivity, has been expressed by the ratio 90th/10th percentile.
The spread due to meteorology and emission is of similar magnitude in the Western Norway case.
The spread due to model formulations is also of the same magnitude as the spread in meteorology and emission.
Following the plume, the SNAP model yields higher concentrations, but lower depositions than DIPCOT
A more in-depth analysis to better understand model differences, is recommended.