## Slide 1
CONFIDENCE WP1
Emergency response and dose assessment: operational recommendations
Peter Bedwell
Irène Korsakissok, Susan Leadbetter, Raphaël Périllat, Csilla Rudas, Jasper Tomas, Joseph Wellings

## Slide 2: Introduction and objectives
The CONFIDENCE WP1 work has provided insight into dealing with uncertainties in emergencies.
However, run times were too long to be of use in real emergency response situations.
To develop an operational method: run time must be reduced.
Specifically: aim to recommend approaches that enable a measure of uncertainty to be obtained within one hour.
Ultimately: improve provision of radiological protection advice in an emergency response.

## Slide 3: How to reduce run time?
In this case, uncertainty arises from atmospheric dispersion modelling using ensembles. So, there are two main options…
  Reduce the number of ensemble members.
  Reduce model run time for individual ensemble members.
But avoid unacceptable detriment to:
  model endpoints derived;
  uncertainty estimated;
  radiation protection advice inferred.

## Slide 4: Why not just run with “worst case” scenario?
 | Primary |  | Secondary |  | Tertiary | 
 | Upper ERL | Lower ERL | Upper ERL | Lower ERL | Upper ERL | Lower ERL
Number evacuated | 5,1 | 4,3 | 5,6 | 4,8 | 5,2 | 4,1
Area evacuated | 5,1 | 5,3 | 5,6 | 5,8 | 5,2 | 5,4
Max distance evacuated | 5,2 | 6,6 | 5,7 | 6,10 | 5,1 | 5,6
Number sheltered | 4,3 | 4,4 | 4,8 | 4,9 | 4,1 | 6,6
Area sheltered | 5,3 | 4,4 | 5,8 | 4,9 | 5,4 | 6,6
Max distance sheltered | 6,3 | 4,4 | 6,9 | 4,9 | 6,8 | 6,6
Number stable iodine | 4,8 | 4,4 | 4,3 | 4,9 | 5,1 | 4,5
Area stable iodine | 5,1 | 4,4 | 5,6 | 4,5 | 6,9 | 4,10
Max distance stable iodine | 6,6 | 6,9 | 6,10 | 6,10 | 5,6 | 6,3
Worst case source term ensemble member and meteorological ensemble member (represented by numeric values) for a range of protective action endpoints and uncertainty descriptors
Case study: REM2 (90 simulations)
where x,y indicates (source term),(meteorology); ERL: UK’s Emergency Reference Levels
What is the worst case? There is no unambiguous answer.

## Slide 5: Investigations (1): reducing the number of ensemble members
Investigation of reducing the number of ensemble members focused mainly on clustering ensemble members.
  Principle: gathering members with similar behaviour (according to a given criterion) and choosing one representative member for each group
Automated clustering using computational algorithms
  Criteria for clustering? Not a simple matter.
  Principal Component Analysis or more sophisticated mathematical methods.
  Ideas: keep the ensemble’s spread, give different weights to different members…
  Issues of high-dimension fields and correlation between variables.
Example of automated reduction of an ensemble of source terms (ST) using PCA
Applied to the REM-long release for 131I
197 ST
10 ST

## Slide 6: Reducing the number of dispersion members: an example of “manual clustering”
Accurately represent the underlying uncertainty
vs.
The least amount of dispersion calculations
Methods:
Clustering of meteorological members (‘members look alike’)
Clustering of source terms (‘source terms look alike’)
What we actually want to achieve:
Clustering of dispersion members (‘dispersion results look alike’)
a priori
selection

## Slide 7: REM2: dispersion member reduction (1)
Dispersion runs |  | 
M | 10 | 1
T | 7 | 6
H | 5 | 5
MTH | 350 | 30
Total | 380 | 
‘Dispersion calculation’
clustering
TIAC I-131>5000 Bq.h.m3
Depo I-131>5000 Bq.m-2
TIAC I-131>5000 Bq.h.m3
Depo I-131>5000 Bq.m-2
10 members
1 member representation
Dispersion runs | 
M | 10
T | 13
H | 5
MTH | 650
Total | 650
“Full” ensemble
“Reduced” ensemble (58%)

## Slide 8: REM2: dispersion member reduction (2)
Dispersion runs |  | 
M | 10 | 1
T | 7 | 6
H | 5 | 5
MTH | 350 | 30
Total | 380 | 
TIAC I-131>5000 Bq.h.m3
Depo I-131>5000 Bq.m-2
TIAC I-131>5000 Bq.h.m3
Depo I-131>5000 Bq.m-2
10 members
1 member representation
Dispersion runs |  | 
M | 10 | 1
T | 5 | 6
H | 5 | 5
MTH | 250 | 30
Total | 280 | 
“Full” ensemble
“Reduced” ensemble (43%)
Dispersion runs | 
M | 10
T | 13
H | 5
MTH | 650
Total | 650

## Slide 9: REM2: dispersion member reduction (3)
Dispersion runs |  | 
M | 3 | 1
T | 7 | 6
H | 5 | 5
MTH | 105 | 30
Total | 135 | 
TIAC I-131>5000 Bq.h.m3
Depo I-131>5000 Bq.m-2
TIAC I-131>5000 Bq.h.m3
3 members
1 member representation
“Full” ensemble
“Reduced” ensemble (21%)
Depo I-131>5000 Bq.m-2
Dispersion runs | 
M | 10
T | 13
H | 5
MTH | 650
Total | 650

## Slide 10: Investigations (2): reducing model run time
Investigation of reducing model run time for an individual ensemble member:
  Where possible: re-run hypothetical scenarios with a simplified model set-up, meteorology, dispersion modelling, etc.
  Compare with analogous unsimplified runs.
  Assess whether simplified set-up allowed a suitable representation of the uncertainty.
  Consider reduction in run-time? Is it worth it?
See example on poster: “Efficiency savings in model setup for an ensemble approach used to describe atmospheric dispersion model uncertainty” (Rudas et al)

## Slide 11: Recommendations
When providing advice in a radiological emergency: use an ensemble approach to describe uncertainty.
The main focus for efficiency savings should be on reducing model run time for a single ensemble member (rather than on reducing the number of ensemble members).
  Reduce the number of model puffs or particles.
  Reduce the size of the model domain, fitted to the key model endpoints
  Reduce the radiological-specific computation:
    Apply a unit release of a subset of pseudo radionuclides, where each is representative of a group of radionuclides (chemical/physical properties).
    Model radionuclides on the basis of a computationally inexpensive approach, then consider only those expected to make a significant contribution to the model endpoints derived.

## Slide 12: Recommendations (continued)
Reducing the time taken to read and process meteorological data
  Investigate the effect of reducing the time/spatial resolution for different types of dispersion models (Gaussian/Eulerian/Lagrangian)
If the above recommendations are insufficient and a large number of ensemble members are being considered: reduce the number of ensemble members.
  Clustering of ensemble members: investigate methods to take into account high-dimension and/or correlated fields
  If possible, clustering should be done with respect to dispersion endpoints and not only a priori (meteorological / release) information!

## Slide 13: Recommendations for operational use (not related to run time)
Consider a range of uncertainty indicators.
  Surface area affected
  Number of people affected
  Maximum distance above a given threshold dose (or environmental concentration)
  Figure of merit in space
  Figure of merit of population
Include level-of-agreement plots and/or percentile plots.
A spread of uncertainty indicators and presentation methods is vital to fully understand model endpoint uncertainties which are spatially and temporally complex.

## Slide 14: Future work
Four main themes for further investigation
  Reducing model run time for a single ensemble member
  Reducing the number of ensemble members by an appropriate selection method
  Use of dispersion field studies to assess the quality of ensemble simulations
  Improvement of input uncertainties, combining a priori knowledge and observational data