## Slide 1
CONCERT Project Website (https://concert-h2020.eu )
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website https://www.eu-neris.net/projects.html
An investigation into the sources of uncertainty of the ERMIN urban dose model
Tom Charnock
Public Health England, Centre for Radiation, Chemical and Environmental Hazards, Didcot, UK
Tom.charnock@phe.gov.uk
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Introduction
Uncertainty investigation
Recommendations for ERMIN development
The ERMIN model was developed to predict residual doses in an urban area with and without clean-up options. It has been implemented within both the RODOS and ARGOS decision support systems. Like all models, it is subject to uncertainty and this poster illustrates an investigation (Charnock, 2018) for the purpose of making recommendations for the development and use of ERMIN. It also illustrates how these technical uncertainties were calculated for some of the CONFIDENCE WP4 panels and the dissemination workshop.
The investigation focussed on the prediction of normal living residual external dose, and on 137Cs in a soluble aerosol form, a form likely in a typical ‘reactor’ accident. Table 1 gives examples of some of the sources of uncertainty that were identified. Sensitivity analysis (SA) and uncertainty analysis (UA) were used to further explore parameter uncertainty; a combination of stochastic and judgemental uncertainty. The parameter distributions for initial surface deposition, retention, soil migration and occupancy proposed by Andersson (2018) were used, supplemented with distributions compiled under the original development of ERMIN. Some examples are given below.
The recommendations arising from this work are:
Incorporate soil/nuclide/particle specific soil migration,
Incorporate different roof materials,
Add new urban environments (especially more built-up), and
Augment the ERMIN indoor deposition model and parameters.
A full discussion can be found in Charnock 2018.
Category | Source examples
Stochastic: related to physical randomness | Relative initial deposition onto urban surfaces, weathering rates, soil migration rates, occupancy.
Judgemental: parameter choice | Choice of ‘representative’, ‘average’ or ‘conservative’ parameters for deposition, weathering, occupancy, clean-up options etc.
Epistemological: lack of knowledge | Reference surface deposition (radionuclide amounts, mix and forms), built environment configuration (e.g. degree of paving), protective action timing etc.
Computational: specific hardware | Grid resolution, temporal step, numerical integration.
Model uncertainty: real world simplification | Choice of urban surfaces, continuous retention functions to represent periodic weathering, grid size, time step, occupancy weighting scheme, leaf-fall.
Ambiguity: lack of clarity and endpoint uncertainty | Occupancy weighting scheme, meaning of ‘other’ paved and composite ‘interior’ surfaces.
The ERMIN model
The main user inputs into ERMIN are:
Initial deposition and forms of radionuclides to lawn reference surface.
Built environment, as fractions of standard urban environments.
The clean-up options applied. • Occupancy: time spent indoors.
The calculation steps are:
Estimate deposition onto all urban surfaces (e.g. roads) with empirical ratios
Calculate surface weathering and soil migration, using empirical functions
Calculate dose-rates from surfaces to indoors and outdoors locations, using factors from Monte Carlo particle transport studies of urban configurations.
Represent clean-up by moving radioactivity and modifying retention.
The outputs include:
Dose-rates and doses indoors and outdoors in various environments
Estimates of ‘normal-living doses’ with and without recovery options
Cost and effort of clean-up • Exposure of clean-up workers (person Sv).
Quantity (kg) and radioactive concentration of waste (Bq kg-1).
Figure 3.
Figure 2.
A deposition of
500 kBq.m-2 gives 5mSv y-1
Figure 4a.
Figure 4b.
Figure 4c. Predicted area still above a RL of 5 mSv y-1 at 1 year
References
Andersson K,G. (2018) Addressing the uncertainties in urban/inhabited scenarios, Appendix 1 Urban Scenario Parameter Uncertainty. EJC CONCERT EURATOM H2020 – 662287, D9.20.
Charnock TW (2018). Addressing the uncertainties in urban/inhabited scenarios, Appendix 2 ERMIN Uncertainty. EJC CONCERT EURATOM H2020 – 662287, D9.20.
ICRP (2009). Application of the Commission's Recommendations to the Protection of People Living in Long-term Contaminated Areas after a Nuclear Accident or a Radiation emergency. ICRP Publication 111. Annals of the ICRP 39(3).
Example 1 – Two initial bench mark runs (Figure 1) illustrate the different doses and relative surface contributions in urban environments and deposition conditions. The SA and UA were repeated for different environments and conditions.
Example 2 – in ERMIN soil migration is modelled with a single set of empirical parameters for all radionuclides and soil types. Figure 2 shows the prediction of the concentration profile of 137Cs at 1 year using migration parameters proposed for three different soil types; clay-loam, sandy and organic, as well as the current ERMIN default soil. Migration impacts on both the residual doses and on the effectiveness of soil-removal clean-up options.
Figure 1.
Example 4 – ICRP recommend that a reference level (RL) of dose is set at the end of the emergency (ICRP 2009), a time when uncertainty on residual doses will be high. To illustrate, factors were calculated combining uncertain occupancy, deposition, retention and urban environment (Figure 4a). When applied to a hypothetical deposition pattern (e.g. Figure 4b), with an arbitrary RL, both the extent and duration that dose exceeds the RL for different percentiles of dose prediction can be compared, as shown in Figure 4c.
Example 3 - Figure 3 shows the impact of roof deposition ratio uncertainty on the total residual dose, with a difference of about 50% between the highest and lowest doses predicted. There are two distinct groups; rougher more pitted materials (clay, concrete and cement) with higher deposition, and smoother materials (glass, metal and silicon covered fibre cement) with lower deposition and subsequent doses.
Table 1.