## Slide 1
CONCERT Project Website (https://concert-h2020.eu )
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website https://www.eu-neris.net/projects.html
New concepts and parameters representing uncertainty in dose estimation for contaminated inhabited areas
Kasper G. Andersson
Technical University of Denmark (DTU), Roskilde, Denmark
kgan@dtu.dk
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Introduction
Conclusion
Results
Before 1986, it was in general thought that any significant airborne environmental contamination resulting from nuclear power plant accidents would be restricted to rural areas very near the power plant. The Chernobyl accident demonstrated that inhabited environments and even cities at considerable distances from the release point could become strongly affected. On the basis of the measurements and learning points after the Chernobyl accident, relatively simple calculation models were soon created to enable rough estimation of the external doses to urban and suburban populations. These models were later integrated with the much more comprehensive map based decision support systems ARGOS (2018) and RODOS (2018), which today support emergency preparedness in practically all European countries as well as in, e.g., Canada, Brazil and Australia. Over the following decades, the common model for external dose in inhabited areas in the ARGOS and RODOS systems, known as the ERMIN (EuRopean Model for INhabited areas) model co-developed between DTU and Public Health England was developed and considerably refined, for example through extended studies of long-term natural weathering parameter components of contaminants on different types of surface, and conceptual improvements (including representation of weather conditions and contaminant characteristics).
Dose estimation tools like ERMIN for are essential for
Rough early phase risk prognoses (when reliable measurements have not yet been made)
Estimation of doses received in a contaminated area over time (recovery justification)
Estimation of possible implications of recovery countermeasures (including residual doses)
Preparedness exercises, drills and training (including evaluation of current preparedness)
The ERMIN model was originally not built for probabilistic assessments. Therefore, an effort was needed in the CONFIDENCE project to introduce new concepts and parametric uncertainty estimates, taking the latest information into account and considering a wider range of case specific parametric options, thus reducing the overall prognostic uncertainty.
Example below: dry deposition relative to that on a well-defined reference surface (based on knowledge from actual measurements).
*Values given per area of ground covered by the vegetation.
Note: typical dry deposition velocities to ref. surface (unit: 10-4 m/s ) are respectively (left to right): 20, 4, 7, 30 and 130.
Material specification can lead to difference in early retention by a factor of 4-5, although all these materials contain large numbers of intact micaceous minerals with caesium traps.
Previously, in ERMIN, the run-off / very early wash-off was assumed to be 50 % with a sd of 30 % (for all contaminants).
The retention after the deposition process is over 15 years for all these materials: half-life of 37 % +/- 6 % years (independent measurements made in different countries: Denmark, Germany, UK)
For example on a glass roof, the weathering process has been found to have a half-life of 95 +/- 20 days. Similar figures have been found for a metal roof.
The above figures are for cationic caesium contamination. Sr-90 (in soluble form) weathering on a clay tile roof has a half-life of only ca. 2 months.
Also contaminants associated with fuel particles are removed very rapidly from any surfaces through natural weathering processes.
There are no specific strong retention traps in clay bricks, which are fired at high temperature compared with roofs (the clay material here becomes amorphous).
However, due to the vertical orientation, contaminant weathering processes on walls normally have a half-life of some 7 +/- 2 years.
Street dust has caesium specific fixation traps, but the dust is not fixed to the surface.
Modelling of migration of contaminants in soil in ERMIN (RODOS/ARGOS):
Vertical migration is described by a one dimensional convective-dispersive, local equilibrium mass transport model.
The crucial parameters are the dispersion coefficient, the mean pore water velocity, the distribution coefficient of the contaminant in the soil (kd), the bulk soil density, and the soil porosity. These depend on soil type. Previously this was not considered in ERMIN, and the dose estimates would thus have been associated with greater uncertainties.
Results of a review of values of Kd for 3 important elements by soil type in different types of soil, based on hundreds (for Cs and I) of field assessments (in units of L/kg = cm3/g).
GM: geometric mean; GSD: geometric standard deviation; AM: arithmetic mean; SD: arithmetic standard deviation.
References (for further reading)
Example
Estimates of kerma /dose rate from different contaminated surfaces in an inhabited environment. Roof contamination is here highly important.
Updated methodologies and data libraries have been created which not only extend the data platform for the traditionally deterministic ERMIN model to become probabilistic with proper parameter uncertainty estimates, but also introduces new measures to reduce uncertainties case specifically. For example, different weathering processes can make expected dose contributions from clay roofs and metal roofs differ by several orders of magnitude.
Hinrichsen, Y. & Andersson, K.G. (2019). European decision support modelling of long-term external doses received in inhabited areas contaminated by a nuclear power plant accident - 1: Initial relative dose rate contributions from different contaminated outdoor surfaces, Journal of Environmental Radioactivity, vol: 204, pages: 143-153, DOI: https://doi.org/10.1016/j.jenvrad.2019.04.008.
Hinrichsen, Y. & Andersson, K.G. (2019). European decision support modelling of long-term external doses received in inhabited areas contaminated by a nuclear power plant accident - 2: Post deposition contaminant mobility on outdoor surfaces, Journal of Environmental Radioactivity, vol: 204, pages: 154-162, DOI: https://doi.org/10.1016/j.jenvrad.2019.04.009.
Charnock, T., Andersson, K., Montero, M. & Trueba, C. (2018). Addressing the uncertainties in urban/inhabited scenarios, EJC CONCERT EURATOM H2020 – 662287, D9.20.